## Slide 1: WF on UE feature list for CA/EN-DC, other capability and LTE-NR co-existence
Intel Corporation
3GPP TSG-RAN WG4 Meeting 86 Athens, Greece, 26 February – 2 March 2018 Agenda Item: 7.1
R4-1803522

## Slide 2: Capabilities for EN-DC/CA

## Slide 3: EN-DC/NR CA capabilities
  RAN4 #86 online agreements (Mon)
During RAN4 #86, continue to discuss overall EN-DC/NR CA capability framework including (aggregated) channel bandwidth, CA bandwidth class, supported SCS and non-contiguous intra-band CA frequency span, etc
The capability of supporting SCS within the single carrier in the CA configuration will be signalled separately, i.e., there is no need to mandatory UE to support mixed numerologies in CA case.
  If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signalling
  Capability signalling for CA case can be further discussed.
Non-contiguous intra-band CA frequency span is applicable only to FR2 (FFS for whether applicable for downlink only or both downlink and uplink)
  Continue to discuss the followings during RAN#86
    Option1: Combine CA bandwidth class, i.e. no dedicated capability
    Option2: Type 1
For Simultaneous reception and transmission for inter band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS.
The capability of asynchronous FDD-FDD intra-band LTE-NR DC is per band combination

## Slide 4: EN-DC/NR CA capabilities
  RAN4 #86 online agreements (Thu)
RAN4 will ask the feasibility of removing certain capability signaling after ASN.1 frozen.
Merge RAN1 feature 0-9 and RAN4 feature 2-2
Inform RAN2 that from RAN4 perspective UE shall be able to signal the supported SCS per CC for each band combination.
For Non-contiguous intra-band CA frequency span, RAN4 shall follow the agreed LS
Split the feature 2-4 into EN-DC and NR-CA. Type 3 capability signalling (per band combination) is applied for both EN-DC and NR-CA. Further discuss in RAN4 86bis whether to mandate this feature for both EN-DC and NR-CA

## Slide 5: Maximum Channel BW
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-1 | Maximum channel bandwidth supported in each band for DL and UL separately and for each SCS that UE supports with a single CC | 1) FR1 channel bandwidths in TS38.101-1 Table 5.3.5-1 2) FR2 channel bandwidths in TS38.101-2 Table 5.3.5-1 |  | Yes | For FR1, all the bandwidths listed in TS38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC For FR2, UE does not support some UE channel bandwidths | Type 1 | No Need | No Need |  | UE capability signalling shall follow RP-172832 (Per-band capability signalling, separately for DL and UL and for each SCS) For FR1, all the bandwidths listed in TS38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC For FR2, the set of mandatory CBW is FFS Overall EN-DC/NR CA capability framework will be discussed in RAN4 #86 | RAN2/4 RAN4 | NA Optional | 

## Slide 6: Mixed numerologies for CA (1)
  Background:
    RAN4 AH 1801 agreements
    Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15
    RAN4 86 agreements (Mon)
    The capability of supporting SCS within the single carrier in the CA configuration will be signalled separately, i.e., there is no need to mandatory UE to support mixed numerologies in CA case.
      If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signalling
      Capability signalling for CA case can be further discussed.
    RAN4 86 agreements (Thu)
      Merge RAN1 feature 0-9 and RAN4 feature 2-2
      Inform RAN2 that from RAN4 perspective UE shall be able to signal the supported SCS per CC for each band combination.
    RAN1 feature list
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
0-9 | Subcarrier spacings and FFT size in conjunction with supportable BW with normal CP | 1) 15kHz 2) 30 kHz 3) 60 kHz 4) 120 kHz |  | Yes |  | Type 4 [Type 3] RAN4 to decide | RAN4 to decide | RAN4 to decide |  | It is up to RAN4 decision Baseband processing (memory) in CA combination related as well as RF (SCS support is per band between sub6 and mmWave) | RAN4 |  | 

## Slide 7: Mixed numerologies for CA (2)
  Proposal (note: agreed aspects are marked green, non-agreed are marked in red)
  Further discuss merged feature description
  Further discuss if clarifications on the BPC signalling needed
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-2 | Mixed numerologies for CA Simultaneous reception or transmission with same or different numerologies in CA | 1) Support simultaneous reception or transmission with same or different numerologies in CA |  | Yes | UE does not support simultaneous reception or transmission with same or different numerologies in CA | Type 3 | No | No |  | From RAN4 perspective UE shall be able to signal the supported SCS per CC for each band combination Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15 The capability of supporting SCS within the single carrier in the CA configuration will be signalled separately, i.e., there is no need to mandatory UE to support mixed numerologies in CA case If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signaling | RAN4 |  | 

## Slide 8: Non-contiguous intra-band CA frequency span
  Background: RAN4 86 agreements
  Non-contiguous intra-band CA frequency span is applicable only to FR2 (FFS for whether applicable for downlink only or both downlink and uplink)
  Continue to discuss the followings during RAN#86
    Option1: Combine CA bandwidth class, i.e. no dedicated capability
    Option2: Type 1
    For Non-contiguous intra-band CA frequency span, RAN4 shall follow the agreed LS
  Proposal (note: agreed aspects are marked green, non-agreed are marked in red)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-3 | Non-contiguous intra-band CA frequency span separation class for FR2 | Support of non-contiguous intra-band CA frequency separation class |  | Yes | UE does not support non-contiguous intra-band CA for FR2 frequency span | Option 1: Combine with CA BW class Option 2: Type 1 | No need | Applicable only to FR2 |  | UE signals the Frequency separation classes with per band granularity (Type 1) based on R4-1803363 Separate Frequency separation classes can be signalled for DL and UL FFS for whether applicable for downlink only or both downlink and uplink | RAN4 |  | 

## Slide 9: Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD)
  Background: RAN4 86 agreements
  For Simultaneous reception and transmission for inter-band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS
  Split the feature 2-4 into EN-DC and NR-CA. Type 3 capability signalling (per band combination) is applied for both EN-DC and NR-CA. Further discuss in RAN4 86bis whether to mandate this feature for both EN-DC and NR-CA
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-4 | Simultaneous reception and transmission for inter-band EN-DC (TDD-TDD or TDD-FDD) | 1) Simultaneous reception and transmission for inter-band EN-DC (TDD-TDD or TDD-FDD) |  | Yes | UE does not support simultaneous reception and transmission for inter-band CA (TDD-TDD or TDD-FDD) | Type 3 | No Need | No Need |  | Per band combination UE capability signalling granularity (Type 3) Whether to mandate this feature in certain band combinations is FFS | RAN4 | TBD | 
2-x | Simultaneous reception and transmission for inter-band CA (TDD-TDD or TDD-FDD) | 1) Simultaneous reception and transmission for inter-band CA (TDD-TDD or TDD-FDD) |  | Yes | UE does not support simultaneous reception and transmission for inter-band CA (TDD-TDD or TDD-FDD) | Type 3 | No Need | No Need |  | Per band combination UE capability signalling granularity (Type 3) Whether to mandate this feature in certain band combinations is FFS | RAN4 | TBD | 

## Slide 10: Asynchronous FDD-FDD intra-band LTE-NR DC
  RAN4 86 agreements
  The capability of asynchronous FDD-FDD intra-band LTE-NR DC is per band combination
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-5 | Asynchronous FDD-FDD intra-band LTE-NR DC EN-DC | Asynchronous FDD-FDD intra-band LTE-NR DC EN-DC |  | Yes | UE does not support asynchronous FDD-FDD intra-band LTE-NR DC EN-DC | Type 3 (Per band combination) | Applicable only to FDD | Applicable only to FR1 |  | Per band combination UE capability signalling granularity (Type 3) | RAN4 | Optional | 

## Slide 11: Other capabilities

## Slide 12: Background
  RAN4 86 agreements (Mon)
    For 60Khz SCS, it is agreed to introduce capability signalling per UE for FR1. Further discussion on the mandatory or optional in this week is needed.
    Remove number of MIMO layers from RAN4 feature list
    No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week.
    Continue to discuss necessity of the capability of BWP switching delay during RAN#86
    Capability signaling for ECP will be Type 4 (per UE) if we introduce the capability signalling. FFS for wehther ECP is mandatory or optional. FFS for whether we need this feature for FR2 pending on the further check from operators in this week.
    Postpone the non-continuous CP-OFDM for uplink feature to June 2018.
    RAN4 can inform the Type 4 (per UE) capability for the feature of PA calibration gap in RAN4 #86 meeting (detailed wording of information can be discussed). RAN4 will further discuss the UE capability in the future. We can revisit the need of calibration gap once RAN4 reach consensus.
    Introduce capability signaling of [non-default] UE power class, and Type 1 (per band) signaling
      FFS: Default power class(es) for FR2. ( different UE device types may have different default power class)
      FFS: Definition under inter-band NR CA and EN-DC
      RAN4 will further discuss the mandatory of PC2 for FR1 in certain region.

## Slide 13: Background
  RAN4 86 agreements (Thu)
    Rename feature to “Almost contiguous UL CP-OFDM”. RAN4 inform RAN2 to introduce Type 4 signalling with per-FR1/FR2 differentiation. RAN4 will continue to discuss whether to introduce the requirements.
    Power Class for FR1 EN-DC and NR CA mode need to be signaled as UE capability
    Power Class for FR1 EN-DC and NR CA is per band combination capability
    RAN4 will continue discuss the missing capability signaling for power class if any in this week

## Slide 14: 60kHz of subcarrier spacing for FR1
  Background: RAN4 86 agreements
    For 60Khz SCS, it is agreed to introduce capability signalling per UE for FR1. Further discussion on the mandatory or optional in this week is needed.
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-1 | 60kHz of subcarrier spacing for FR1 | 1) 60kHz subcarrier spacing for data channel in FR1 |  | Yes | UE does not support 60kHz of subcarrier spacing for data channel in FR1 | Type 4 | No Need | Applicable only to FR1 |  |  | RAN4 | TBD | 

## Slide 15: Extended CP
  Background:
    RAN4 86 agreements: Capability signaling for ECP will be Type 4 (per UE) if we introduce the capability signalling. FFS for whether ECP is mandatory or optional. FFS for whether we need this feature for FR2 pending on the further check from operators in this week.
    RAN1 agreements: Optional with capability signalling
  Proposal
  Keep the feature in the RAN1 feature list. Remove “Extended CP” from the RAN4 UE feature list.
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-2 | Extended CP | 1) Extended CP | Only for UE that supports 60kNHz SCS | Yes | UE does not support extended CP | Type 4 if needed | No need | TBD |  |  | RAN4 | TBD | 

## Slide 16: PA Calibration Gap (1)
  Background:
    RAN4 AH 1801 agreements
      The need for UE calibration gap is a UE capability
        The capability definition is per UE as a baseline assumption
        Companies are encouraged to provide additional analysis whether a per-band definition is needed or if the baseline assumption can be confirmed next meeting
    RAN4 86 agreements
      RAN4 can inform the Type 4 (per UE) capability for the feature of PA calibration gap in RAN4 #86 meeting (detailed wording of information can be discussed). RAN4 will further discuss the UE capability in the future. We can revisit the need of calibration gap once RAN4 reach consensus.
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Introduce Type 4 (per UE) UE capability signaling of PA Calibration gap (PCG)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-7 | PA calibration gap | 1) Support of PA calibration gap to implement PA digital pre-distortion techniques |  | Yes | UE does not support PA calibration gap | Type 4 | No Need | Applicable only to FR2 |  | RAN4 will further discuss the UE capability in the future. Can revisit the need of calibration gap once RAN4 reach consensus. | RAN4 | Optional | 

## Slide 17: Non-contiguous UL CP-OFDM
  Background: RAN4 86 agreements
    Postpone the non-continuous CP-OFDM for uplink feature to June 2018.
    Rename feature to “Almost contiguous UL CP-OFDM”. RAN4 inform RAN2 to introduce Type 4 signalling with per-FR1/FR2 differentiation. RAN4 will continue to discuss whether to introduce the requirements.
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-6 | Almost contiguous UL CP-OFDM | 1) Support of almost contiguous UL CP-OFDM transmissions |  | Yes | UE cannot support almost contiguous UL CP-OFDM transmissions | Type 4 | No | Yes |  | RAN4 will continue to discuss whether to introduce the requirements. | RAN4 |  | 

## Slide 18: UE Power Class (1)
  Background: RAN4 86 agreements
    RAN4 86 agreements (Mon)
      Introduce capability signaling of [non-default] UE power class, and Type 1 (per band) signaling
        FFS: Default power class(es) for FR2. ( different UE device types may have different default power class)
        FFS: Definition under inter-band NR CA and EN-DC
        RAN4 will further discuss the mandatory of PC2 for FR1 in certain region.
    RAN4 86 agreements (Thu)
      Power Class for FR1 EN-DC and NR CA mode need to be signaled as UE capability
      Power Class for FR1 EN-DC and NR CA is per band combination capability
      RAN4 will continue discuss the missing capability signaling for power class if any in this week
  Proposal
    Capability signalling
      FR1 UE power class ( Type 1 (per band))
      FR2 UE power class ( Type 1 (per band))
      FR1 UE power class for EN-DC and NR CA (Type 3 (per band combination))
        Do we need to separate capabilities for EN-DC and NR CA power classes?
      Notes:
        FR1 UE power class: Signaling provided for non-default UE power class only
        FR2 UE power class:
          Option 1: Signaling provided for UE power class
          Option 2: Signaling provided for non-default UE power class
        Number of possible values for each power class: up to [16]

## Slide 19: Capabilities for LTE/NR coexistence

## Slide 20: Background
RAN4 86 agreements (Mon)
  7.5kHz UL raster shift is mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective
  Further discussion on supporting 7.5kHz UL raster shift for LTE-NR co-existence for Band n2, n5 and n66.
  It is common understanding that some UE support UL sharing from UE perspective and some UE does not support UL sharing from UE perspective, UE need to indicate the supports to the network. For UE supporting UL sharing from UE perspective, the capability signaling type for “Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective” shall be per band combination
  Continue discuss on the feature 1-14, 1-15 and 1-16 in this meeting.

## Slide 21: Background
RAN4 86 agreements (Thu)
  Introduce Type 1 capability signalling for 7.5 kHz UL raster shift. RAN4 will continue discuss the decision of recommendation of mandatory or optional of feature in this week. If RAN4 agreed to recommend this feature as mandatory without signalling, the capability signalling will be removed from the LS to RAN2.
  For Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective, UE Capability signalling shall be type 3 (per band combination). UE Capability signalling elements. Capability 1: ~0us switching type. Capability 2: <20us switching type.
  Keep feature ‘Support of UL sharing from UE perspective’. The capability signaling type is type 3 (per band combination).
  Prerequisite feature groups of feature 1-12 is 1-11
  Remove “Supplemental uplink features” from RAN4 discussion since this feature will be discussed RAN1 feature.

## Slide 22: 7.5kHz UL raster shift
RAN4 86 agreements
  Mon: 7.5kHz UL raster shift is mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective. Further discussion on supporting 7.5kHz UL raster shift for LTE-NR co-existence for Band n2, n5 and n66.
  Thu: Introduce Type 1 capability signalling for 7.5 kHz UL raster shift. RAN4 will continue discuss the decision of recommendation of mandatory or optional of feature in this week. If RAN4 agreed to recommend this feature as mandatory without signalling, the capability signalling will be removed from the LS to RAN2.
  Proposal
    Further discuss if prerequisite feature group needed
    7.5kHz UL raster shift is mandatory in Bands n1, n2, n3, n5, n7, n8, n20, n28, n66. RAN4 can revisit the above bands in the future release.
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-13 | 7.5kHz UL raster shift | 1) 7.5kHz UL raster shift | [1-11] | Yes | UE does not support 7.5kHz UL raster shift | [Type 1] | N/A | Applicable to FR1 only |  |  | RAN4 | Mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective 7.5kHz UL raster shift is mandatory in Bands n1, n2, n3, n5, n7, n8, n20, n28, n66. RAN4 can revisit the above bands in the future release. | 

## Slide 23: Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective
RAN4 86 agreements (Thu)
  For Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective, UE Capability signalling shall be type 3 (per band combination). UE Capability signalling elements. Capability 1: ~0us switching type. Capability 2: <20us switching type.
Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-12 | Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective | Support of switching type between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective. Type 1: ~0us Type 2: <20us | 1-11 | Yes | UE does not support UL subcarrier alignment between LTE and NR for EN-DC with LTE-NR coexistence in UL | Type 3 | No Need | Applicable only to FR1 |  | Per band combination signalling (Type 3) UE Capability signalling elements. 1: ~0us switching type. 2: <20us switching type. | RAN4 | TBD | 

## Slide 24: Support of UL sharing from UE perspective
RAN4 86 agreements (Thu)
  Keep feature ‘Support of UL sharing from UE perspective’. The capability signaling type is type 3 (per band combination).
  Prerequisite feature groups of feature 1-12 is 1-11
  Proposal
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-11 | Support of UL sharing from UE perspective | 1) Support of UL sharing from UE perspective |  | Yes | UE does not support UL sharing from UE perspective | Type 3 | No Need | Applicable only to FR1 |  | The capability signaling type is type 3 (per band combination). | RAN4 | Optional | 

## Slide 25: Supplemental uplink features
  RAN1 feature list
RAN4 86 agreements (Thu)
  Remove “Supplemental uplink features” from RAN4 discussion since this feature will be discussed RAN1 feature.
Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
6-15 | Yes | UE will not be able to perform the RACH/PUSCH/PUCCH/SRS operation in a band combination including SUL | Type 2 or 4 |  |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  | 
6-16? | Yes | The UE will not be able to access or operate on a SUL carrier | Type 2 or 4 | Need Support not required for an FDD-only UE |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  | 
6-16, 6-17? | Yes |  | Type 2 or 4 | Need Support not required for an FDD-only UE |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  |