## Slide 1: Wayforward on requirement of intra-frequency measurement without gap
Mediatek
3GPP TSG-RAN WG4 RAN#86 Bis
Melbourne, Australia, April 16th- 20th, 2018
R4-1803670
Document for: Approval

## Slide 2: Background : requirement of Intra-frequency measurement without gap agreed in #86
Sub-Issue | 
Intra-frequency PSS/SSS Sync. | Agreement: FR1 max(600ms,[5 or 6]x SMTC period) FR2 max([X1]ms,[5 or 6]x N1x SMTC period) Editor’s note: The values of X1, and N1 are to be updated.
Intra-frequency SBI Acquisition | Agreement: FR1 max(120, 3 x SMTC period) FR2 max([X2], [5] x N2 x SMTC period) Editor’s note: The values of X2, and N2 are to be updated.
Intra-frequency Measurement | Agreement: FR1 max(200, 5 x SMTC period) FR2 max([X3], 5 x N3 x SMTC period) Editor’s note: The values of X3, and N3 are to be updated.
  Agreement for single frequency layer

## Slide 3: Background : agreed measurement types in R4-1801829
All the UE activities for consideration (all the activities are SSB based)
  RLM
  Measurement type A: Intra-frequency measurement w/o MG and w/o interruption
    For FR1, no mixed numerologies is assumed for this measurement type
    For FR2, this measurement type is not applicable
  Measurement type B: intra-frequency measurement with interruption
    For FR1, mixed numerologies is assumed for this measurement type
    For FR2, Rx beam sweeping is assumed for this measurement type
  Measurement type C: intra-frequency measurement with MG
    E.g. Intra-frequency measurement outside active BWP
  Measurement type D: inter-frequency measurement and inter-RAT measurement

## Slide 4: Background : agreed measurement types in R4-1801829
  All the scenarios for consideration
    Fully overlapped scenarios:
      Scenario 1a: Fully overlapped between MG and SMTC in type A
      Scenario 1b: Fully overlapped between MG and SMTC in type B
      Scenario 1c: Fully overlapped between MG and RLM
    Partial overlapped scenarios:
      Scenario 2a: Partial overlapped between MG and SMTC in type A
      Scenario 2b: Partial overlapped between MG and SMTC in type B
      Scenario 2c: Partial overlapped between MG and RLM
    Fully non-overlapped scenarios:
      Scenario 3a: Fully non-overlapped between MG and SMTC in type A
      Scenario 3b: Fully non-overlapped between MG and SMTC in type B
      Scenario 3c: Fully non-overlapped between MG and RLM
  In partial overlapped scenarios 2a/2b/2c, the requirements can be further divided into 9 cases
FR1/FR2 | Within MG only | within/outside MG | Outside MG only
2a(Type A) | NA for FR1 (Note-1) | FFS for FR1 (Note-1) | FFS for FR1 (Note-1)
2b(Type B) | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
2c(RLM) | NA for FR1/FFS for FR2 | FFS for FR1/FFS for FR2 | FFS for FR1/FFS for FR2
*Note-1: There is no Type-A measurement in FR2, hence the corresponding requirements aren’t needed |  |  | 

## Slide 5: Scope of this Wayforward
Discuss the requirement considering
  Multiple NR serving cells
  Collision between SMTC occasions and MG
    Scenarios to be first focused on
      2a and 2b when measurement is conducted only outside the MG.
        The requirement for “2a and 2b when measurement can also be conducted within the MG” can be later extended, if RAN4 reaches consensus on whether to specify the corresponding requirements
      The requirements of 3a can be simplified from that of 2a
    Other scenarios to be discussed after RAN4 reaches consensus on whether to specify the corresponding requirements
      1a and 1b
      3b

## Slide 6
  The requirement of single frequency layer is further scaled by the parameter Kca which is a carrier-specific scaling factor, considering the multiple frequency layers
    Kca = 1, for the target frequency layer with NR PCell and NR PSCell.
    Kca = [TBD], for the target frequency layers with NR SCells.
      The value may refer to the RAN4 conclusion on scaling/grouping rules of inter-frequency measurement.
Requirement with multiple NR serving cells (CA/EN-DC)

## Slide 7
  The carrier-specific scaling factor Kca is multiplied with
    Option 1: inside the max function
    Option 2: outside the max function
Requirement with multiple NR serving cells (examples for information)
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 max(600ms, Kcax [5 or 6]x SMTC period) | A, B
 | FR2 max([X1]ms, Kcax [5 or 6]x N1x SMTC period) | B
Intra-frequency SBI Acquisition | FR1 max(120, Kcax 3 x SMTC period) | A, B
 | FR2 max([X2], Kcax [5] x N2 x SMTC period) | B
Intra-frequency Measurement | FR1 max(200, Kcax 5 x SMTC period) | A, B
 | FR2 max([X3], Kcax 5 x N3 x SMTC period) | B
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 max(600ms, [5 or 6]x SMTC period) x Kca | A, B
 | FR2 max([X1]ms, [5 or 6]x N1x SMTC period) x Kca | B
Intra-frequency SBI Acquisition | FR1 max(120, 3 x SMTC period) x Kca | A, B
 | FR2 max([X2], [5] x N2 x SMTC period) x Kca | B
Intra-frequency Measurement | FR1 max(200, 5 x SMTC period) x Kca | A, B
 | FR2 max([X3], 5 x N3 x SMTC period) x Kca | B

## Slide 8
  When intra-frequency measurements are performed in SMTC occasions not overlapped with the gaps
    Requirements for for a single serving cell is scaled by the parameter Kp-intra
      Kp-intra is a scaling factor multiplied with required sample number and then rounded up
      Kp-intra = 1/(1- SMTC period /MGRP), where SMTC period < MGRP
  When intra-frequency measurements can also be performed in SMTC occasions overlapped with the gaps
    Whether to specify the requirement is FFS
Requirement of 2a and 2b when measurement is conducted only outside the MG
Sub-Issue | Requirement | Applicable measurement type
Intra-frequency PSS/SSS Sync. | FR1 max(600ms, Ceil(Kp-intrax [5 or 6])x SMTC period) | A, B
 | FR2 max([X1]ms, Ceil(Kp-intrax [5 or 6]x N1) x SMTC period) | B
Intra-frequency SBI Acquisition | FR1 max(120, Ceil(Kp-intrax 3) x SMTC period) | A, B
 | FR2 max([X2], Ceil(Kp-intrax [5] x N2 ) x SMTC period) | B
Intra-frequency Measurement | FR1 max(200, Ceil(Kp-intrax 5) x SMTC period) | A, B
 | FR2 max([X3], Ceil(Kp-intrax 5 x N3 ) x SMTC period) | B