## Slide 1: LTE-CA, EN-DC, NR CA/DC configuration handling for Rel-16
NTT DOCOMO, INC.
R4-1804570
3GPP TSG-RAN4 Meeting #86bis
Melbourne, Australia, 16th Apr 2018 - 20th Apr 2018

## Slide 2: LTE-CA basket WIs from Rel-16
In principle, any new proposed LTE-CA configurations will be placed into one of the following basket WIs.
  Note that Rel16 LTE CA RRM and UE demodulation is common to any LTE-CA configurations.
    That will be established depending on if the basket WI more than 5CC is completed in Rel15 or not.
# | WI title | rapporteur | company | Email
1 | Rel-16 Intra-band CA for x CC DL/ y CC UL including contiguous and non-contiguous spectrum (x>=y) | [Per Lindell] | [Ericsson] | per.lindell@ericsson.com
2 | Rel16 LTE inter-band CA for 2 bands DL with 1 band UL |  | Qualcomm | 
3 | Rel16 LTE inter-band CA for 3 bands DL with 1 band UL | [Zhangqian] | Huawei | zhangqian67@HUAWEI.COM
4 | Rel16 LTE inter-band CA for 4 bands DL with 1 band UL | [Per Lindell] | [Ericsson] | per.lindell@ericsson.com
5 | Rel16 LTE inter-band CA for 5 bands DL with 1 band UL | [Iwajlo Angelow] | [Nokia] | iwajlo.angelow@nokia.com
6 | Rel16 LTE inter-band CA for 2 bands DL with 2 bands UL | [Leo Liuye] | [ Huawei] | leo.liuye@huawei.com
7 | Rel16 LTE inter-band CA for x bands DL with 2 band UL CA with x=3, 4, 5 | [Lim Suhwan] | [LGE] | suhwan.lim@lge.com
8 | Rel16 LTE CA RRM and UE demodulation | TBD | TBD | 

## Slide 3: EN-DC, NR CA/DC basket WIs from Rel-16
In principle, any new proposed EN-DC configurations will be placed into one of the following basket WIs. Additional baskets can be generated if necessary.
# | WI title | rapporteur | company | Email
1 | NR intra band CA for xCC DL/yCC UL including contiguous and non-contiguous spectrum (x>=y) | [Per Lindell] | [Ericsson] | per.lindell@ericsson.com
2 | EN-DC for 2 bands DL with 2 bands UL(1 LTE band + 1 NR band ) | [Oguma Yuta] | [NTT DOCOMO] | 
3 | EN-DC for 3 bands DL with 2 bands UL(2 LTE bands + 1 NR band ) | [Ye Liu] | [Huawei] | leo.liuye@huawei.com
4 | EN-DC for 4 bands DL with 2 bands UL(3 LTE bands + 1 NR band ) | [Per Lindell] | [Ericsson] | per.lindell@ericsson.com
5 | EN-DC for 5 bands DL with 2 bands UL(4 LTE bands + 1 NR band ) | [Petri Vasenkari] | [Nokia] | Petri.vasenkari@nokia.com
6 | EN-DC for 6 bands DL with 2 bands UL(5 LTE bands + 1 NR band ) | [Yankun Li] | [Samsung] | yankun.li@SAMSUNG.COM
7 | NR Inter-band CA/DC for 2 bands DL with up to 2 bands UL #For NR DC, the basket will be used for NR DC only after the DC configurations selected for late drop is finished. | [Aijun Cao] | [ZTE] | cao.aijun@zte.com.cn
8 | EN-DC of LTE inter band CA for x bands DL with 1 band UL (x=1, 2, 3, 4) + NR inter-band CA for 2 bands DL with 1 band UL | [Suhwan Lim] | [LGE] | suhwan.lim@lge.com

## Slide 4: Handling of configurations not completed by June
Any configurations for LTE-CA, NR CA/DC, EN-DC not completed by June will be moved to one of the basket WIs Rel-16 based on requests using official format.
The deadline of the requests is 10:59pm UTC on Fri 11th May 2018
  There are some conditions to request certain configurations. See slide 6 and 8.
  If the contact persons have configurations which may or may not be completed by May, it is recommended to share the request including the configurations.
  In case the configurations are competed by May, that will be specified in Rel15 even if the contact person share the request for Rel16 basket WI.
The potential rapporteurs will reflect the requests into the respective WIDs before the meeting.
The WIDs will be initially reviewed in the May meeting and endorsed.
The rapporteurs will share revised WIDs based on the outcome of the meeting by the end of Tue 29th May
  Note: Some configurations may be deleted due to unexpected good progress. That means the requirements for the configurations to be deleted from Rel16 WID is specified in Rel15 spec.
The revised WIDs will be further reviewed on 3GPP_TSG_RAN_WG4@LIST.ETSI.ORG by the end of the Fri 1st June and endorsed.

## Slide 5: A way for requests
E-mail reflector for requests
  LTE-CA configurations request: use 3GPP_TSG_RAN_WG4_CA@LIST.ETSI.ORG
  EN-DC, NR CA/DC configuration: use 3GPP_TSG_RAN_WG4_NR_BANDS@LIST.ETSI.ORG
E-mail title: [Request for R4#XX] New configurations by “Company name”
  “[Request for R4#87] New configurations by NTT DOCOMO, INC.”
Request format: use the attachments
  Request sheet for LTE-CA:
  Request sheet for EN-DC, NR CA/DC:
  Note: Requests including information with [ ] will NOT be counted as request
Others
  The proponents shall check if the fallback modes for the proposed configurations have been already specified or not. If NOT, they shall request not specified fallback modes as well.
  An example of a possible WID is attached where the request for 6DL/1UL of CA_3A-28A-41C-42C from SoftBank Corp. in [R4-1802426] is already reflected. Note some missing information should be shared by SoftBank Corp..

## Slide 6: Scope of new LTE-CA basket WIs
# | WI title | Examples
1 | Rel-16 Intra-band CA for x CC DL/ y CC UL including contiguous and non-contiguous spectrum (x>=y) | Any type of intra band CA such as contiguous , non-contiguous, mixed Intra band contiguous and non-contiguous CA configuration (DL, UL)=(1A-1C, 1C)
2 | Rel16 LTE inter-band CA for 2 bands DL with 1 band UL | Any type of inter band CA for x bands with 1 band UL including any type of intra band CA except for intra non-contiguous 2UL (DL, UL)=(3A-42A, 3A or 42A) (DL, UL)=(3A-42C, 3A or 42A or 42C) (DL, UL)=(3A-42A-42C, 3A or 42A or 42C)
3 | Rel16 LTE inter-band CA for 3 bands DL with 1 band UL | 
4 | Rel16 LTE inter-band CA for 4 bands DL with 1 band UL | 
5 | Rel16 LTE inter-band CA for 5 bands DL with 1 band UL | 
6 | Rel16 LTE inter-band CA for 2 bands DL with 2 bands UL | Any type of inter band CA for 2 bands with 2 band UL including any type of intra band CA except for intra non-contiguous 2UL (DL, UL)=(1A-3C, 1A-3A or 1A-3C)
7 | Rel16 LTE inter-band CA for x bands DL with 2 band UL CA with x=3, 4, 5 | Any type of inter band CA for x bands with 1 band UL including any type of intra band CA except for intra non-contiguous 2UL (DL, UL)=(1A-3A-19A, 1A-3A or 1A-19A or 3A-19A) (DL, UL)=(1A-3C-19A, 1A-3A or 1A-3C or 1A-19A or 3A-19A, 3C-19A)
8 | Rel16 LTE CA RRM and UE demodulation | In case CA configurations with the number of CCs more than x CCs is proposed in Rel-16, RRM and demodulation requirements will be addressed in this basket WI. X is FFS. In case of the currently available basket WI for more than 5 CC is completed in Rel15, then, that means RRM and demodulation requirements for up to 7 CCs will be completed. Hence X becomes 7 while it is not completed, then, X will become 5.

## Slide 7: Conditions for request LTE-CA
# | WI title | Conditions: the followings shall be completed or being to be completed in advance
1 | Rel-16 Intra-band CA for x CC DL/ y CC UL including contiguous and non-contiguous spectrum (x>=y) | In case UL CA of x CC DL/y CC UL is proposed, the condition is completion of x CC DL/ (y-1) CC UL. Example: When Intra band contiguous CA of 3cc DL/3ccUL CA is proposed, Intra band contiguous CA of 3ccDL/2ccUL CA shall be completed or being to be completed in advance.
2 | Rel16 LTE inter-band CA for 2 bands DL with 1 band UL | Included intra CAs if any Example: When (DL, UL)=(1A-3C-5A, 1A or 3C or 5A) is proposed, Intra band contiguous CA of (UL, DL) = (3C, 3C) shall be completed or being to be completed in advance..
3 | Rel16 LTE inter-band CA for 3 bands DL with 1 band UL | 
4 | Rel16 LTE inter-band CA for 4 bands DL with 1 band UL | 
5 | Rel16 LTE inter-band CA for 5 bands DL with 1 band UL | 
6 | Rel16 LTE inter-band CA for 2 bands DL with 2 bands UL | All the fallback for 2 bands DL with 1 band UL
7 | Rel16 LTE inter-band CA for x bands DL with 2 band UL with x=3, 4, 5 | Respective inter-band CA for 2 bands DL with 2 bands UL configurations used in a inter-band CA for x bands DL with 2 band UL shall be completed or being to be completed in advance. Example: When (1A-2A-3A, 1A-2A or 1A-3A or 2A-3A) is proposed, (1A-2A, 1A-2A), (1A-3A, 1A-3A) and (2A-3A) shall be completed or being to be completed in advance.
8 | Rel16 LTE CA RRM and UE demodulation | 
The conditions are very similar to what we have had in [RP-162512]
  Common to all baskets: Requirements for operating bands constituent CA configurations should be completed or being to be completed in advance.
  In case new band is specified, the below conditions do not apply. Realistic and reasonable planning however, need to be discussed when that band is being specified.

## Slide 8: Scope of EN-DC, NR CA/DC basket WIs
# | WI title | Examples
1 | NR intra band CA for xCC DL/yCC UL including contiguous and non-contiguous spectrum | Any type of intra band CA such as contiguous , non-contiguous, mixed Intra band contiguous and non-contiguous CA configuration (DL, UL)=(n260A-n260D, n260A or n260D or n260A-n260A or n260A-n260D)
2 | EN-DC for 2 bands DL with 2 bands UL(1 LTE band + 1 NR band ) | Any type of EN-DC for x bands DL with 2 bands UL ((x-1)LTE bands + 1NR band) including any type of LTE/NR intra band CA except for intra non-contiguous 2UL x=up to 6 (DL, UL)=(3A_n78A, 3A_n78A) (DL, UL)=(3A_n78C, 3A_n78A or 3A_n78C) (DL, UL)=(3C_n78A, 3A_n78A or 3C_n78A) (DL, UL)=(3A_n260A-n260A, 3A_n260A or 3A_n260A-n260A)
3 | EN-DC for 3 bands DL with 2 bands UL(2 LTE bands + 1 NR band ) | 
4 | EN-DC for 4 bands DL with 2 bands UL(3 LTE bands + 1 NR band ) | 
5 | EN-DC for 5 bands DL with 2 bands UL(4 LTE bands + 1 NR band ) | 
6 | EN-DC for 6 bands DL with 2 bands UL(5 LTE bands + 1 NR band ) | 
7 | NR Inter-band CA/DC for 2 bands DL with up to 2 bands UL | Any type of NR CA/DC for 2 bands DL with 2 bands UL including any type of NR intra band CA except for intra non-contiguous 2UL (DL, UL)=(n1A-n3A, n1A or n3A or n1A-n3A) (DL, UL)=(n1C-n3A, n1A or n1C or n1A-n3A or n1C-n3A)
8 | EN-DC of LTE inter band CA for x bands DL with 1 band UL (x=1, 2, 3, 4) + NR inter-band CA for 2 bands DL with 1 band UL | Scope depends on the scope of “LTE inter band CA for x bands DL with 1 band UL” and “LTE inter band CA for x bands DL with 1 band UL” (DL, UL)=(1A_n78A-n257A, 1A_n78 or 1A_n257A) (DL, UL)=(1A_n78A-n257F, 1A_n78 or 1A_n257A or 1A_n257D or 1A_n257F)

## Slide 9: Conditions for request EN-DC, NR CA/DC
# | WI title | Conditions: the followings shall be completed or being to be completed in advance
1 | NR intra band CA for xCC DL/yCC UL including contiguous and non-contiguous spectrum | In case UL CA of x CC DL/y CC UL is proposed, the condition is completion of x CC DL/ 1 CC UL. Ex: In order to propose (DL, UL)=(n3A-n3A, n3A-n3A), completion of (DL, UL)=(n3A-n3A, n3A) is the condition.
2 | EN-DC for 2 bands DL with 2 bands UL(1 LTE band + 1 NR band ) | The completion of LTE band and NR band requirements
3 | EN-DC for 3 bands DL with 2 bands UL(2 LTE bands + 1 NR band ) | - All the constituent LTE inter-band CA - Each EN-DC of 1 LTE band + 1 NR band configuration used in a certain x bands DL with 2 bands UL Ex: If (DL, UL)=(1A-3A_n78, 1A_n78 or 3A_n78) is proposed, completion of CA_1A-3A, DC_1A_n78 and DC_3A_n78 is the condition.
4 | EN-DC for 4 bands DL with 2 bands UL(3 LTE bands + 1 NR band ) | 
5 | EN-DC for 5 bands DL with 2 bands UL(4 LTE bands + 1 NR band ) | 
6 | EN-DC for 6 bands DL with 2 bands UL(5 LTE bands + 1 NR band ) | 
7 | NR Inter-band CA/DC for 2 bands DL with up to 2 bands UL | Completion of NR bands is the condition.
8 | EN-DC of LTE inter band CA for x bands DL with 1 band UL (x=1, 2, 3, 4) + NR inter-band CA for 2 bands DL with 1 band UL | - LTE inter-band CA for x bands DL with 1 band UL - NR inter band CA for 2 bands DL with 1 band UL - Each EN-DC of 1 LTE band + 1 NR band configuration used in a configuration shall be specified in advance. Ex: If (DL, UL)=(1A-3A_n5-n78, 1A_n5, 1A-n78, 3A-n5 or 3A_n78) is proposed, completion of CA_1A-3A, CA_n5-n78, DC_1A_n5, DC_1A-n78, DC_3A-n5 and DC_3A_n78 is the condition.
The conditions are very similar to what we have had in [RP-162512]
  Common to all baskets: Requirements for operating bands constituent EN-DC, NR CA/DC configurations should be completed or being to be completed in advance.
  In case new band is specified, the below conditions do not apply. Realistic and reasonable planning however, need to be discussed when that band is being specified.