## Slide 1: Way forward on SSB-based inter-frequency measurement requirements
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.9.4.2
R4-1804748

## Slide 2: Background
Measurement objects with same SMTC periodicity and offset within the same FR range should share the same delay requirement.
Strive to address the SMTC overlapping issue should be based on SMTC periodicity and offset grouping and each group has its own scaling factor
  The definition of SMTC periodicity and offset grouping is FFS
  When all SMTC occasions are non colliding (no measurement gap contains SMTC from more than one frequency layer) there is no need for an additional scaling factor
Strive to keep UE measurement flexibility the same as LTE
Companies are encouraged to suggest the principle to define the requirement methodologies within the below options:
  Option 1: unified delay requirement among different carriers
  Option 2: requirements are defined per carrier
Companies are encouraged to provide views on the impact of AGC issue
FFS the delay caused by gap sharing with intra-frequency measurement and DRX mode.

## Slide 3: Way forward
A per-carrier scaling scheme is suggested for defining inter-frequency measurement requirements within the same gap pattern. Assuming that there are totally Nfreq inter-frequency layers to be monitored via this gap pattern, the requirement of inter-frequency carrier #i can be expressed as:
      Tinter, carrier_i = M×MAX(SMTCcarrier_i, MGRP) × Nscaling,carrier_i , i=1,2…Nfreq.
  M stands for the required sample number for inter-frequency measurement.
    Companies are encouraged to provide views on the impact of AGC issue on the M value
  Nscaling,carrier_i is the scaling factor of carrier #i and Nscaling,carrier_i ≤ Nfreq
  When all SMTC are non colliding (no measurement gap contains SMTC from more than one frequency layer) then Nscaling,carrier_i =1, for i=1,2…Nfreq
  Companies are encouraged to suggest the principle to decide the value of Nscaling,carrier_i
    For any inter-frequency carrier #i and inter-frequency carrier #j,
      If SMTC periodicity and offset of these two inter-frequency carriers are the same, then Nscaling,carrier_i = Nscaling,carrier_j
    The value of Nscaling,carrier_i is suggested to consider the number and SMTC periodicity and offset of carriers whose SMTC occasions are fully or partially colliding with the SMTC occasions of carrier #i.
  Note1: Above requirement does not yet consider the delay caused by gap sharing with intra-frequency measurement and DRX mode.
  Note2: The value of Nscaling,carrier_i is suggested to consider the number of interRAT carriers configured in the UE

## Slide 4: Way forward
Definition of SMTC periodicity and offset set for an inter-frequency carrier are proposed as:
  SMTC periodicity for an inter-frequency carrier equals to the maximum value between the configured SMTC period and MGRP.
  SMTC offset set for an inter-frequency carrier is a set of measurement gap index within a certain 160ms time period, where the measurement gap contains SMTC for this inter-frequency carrier.
Two inter-frequency carrier are considered as being overlapped when the following condition is satisfied:
  The SMTC offset set of one inter-frequency carrier is a sub-set of the SMTC offset set of the other inter-frequency carrier, or
  The SMTC offset set of one inter-frequency carrier is same as the SMTC offset set of the other inter-frequency carrier.