## Slide 1: Way forward on RRM requirements for R15 V2X CA
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 6.16.3
R4-1804798

## Slide 2: Agreements on V2X Carrier Aggregation
V2X Synchronization Reference Source selection/reselection requirements for V2X sidelink CA
  UE is allowed to drop its V2X sidelink transmissions on all the aggregated carriers for the purpose of selection/reselection to the SyncRef UE.
  The existing dropping rate requirements for R14 V2X can be reused for R15 V2X CA
Delay and interruption requirements for V2X CC addition/release are only applied in the scenario that the operation for V2X CC addition/release will not exceed UE Rx/Tx capability limitation.
Interruptions for V2X CC addition/release based on dedicated RRC signaling in sidelink transmission mode 3
  No need to introduce the requirements of interruptions to V2X sidelink communication due to V2X CC addition or release.
  The interruptions to WAN is allowed only during the RRC reconfiguration procedure.

## Slide 3: Agreements on V2X Carrier Aggregation
Delay requirements for V2X CC addition/release
  The CC addition delay can be defined as Tconfig_add_V2X_CC:
    Tconfig_add_V2X_CC = TRRC_process + TRF_operation + TPSSCH_DU
    Where:
    TRRC_process is the RRC processing time and is up to 20ms;
    TRF_operation is the RF operation time which allows UE to perform RF tuning and AGC settling. TRF_operation is up to 1ms.
    TPSSCH_DU is the delay uncertainty in acquiring the first available PSSCH occasion on the added carrier. TPSSCH_DU is up to 100ms.
  The CC addition delay can be defined as Tconfig_rel_V2X_CC:
    Tconfig_rel_V2X_CC = TRRC_process + TRF_operation + TPSSCH_DU
    Where:
    TRRC_process is the RRC processing time and is up to 20ms;
    TRF_operation is the RF operation time which allows UE to perform RF retuning and AGC settling. TRF_operation is up to 1ms.
    TPSSCH_DU is the delay uncertainty in stopping PSSCH transmission on the released carrier. TPSSCH_DU is up to 100ms.