## Slide 1: New work split between RAN4 and RAN5 on NR UE specifications (38.101-1/2/3/4)
Agenda Item: 7.5.10, 7.12.1
Source: Ericsson
Document for: Approval
3GPP TSG-RAN WG4 Meeting #87
Busan, 21st– 25th May, 2018
R4-1806121

## Slide 2: Background
The RMC related test parameters are not taken as high priority in RAN4 as they are more testing related and specified in Annex, instead of specified in core spec with specific chapters.
Many issues identified by RAN5 related to RMC
    For eLAA RAN4 missed to define UL RMCs
    For NB-IoT RMC for RF tests with LS from RAN5 RP-162346 where the scheduling information for UL and DL sub-frame configuration in NB-IoT RMC is missing from RAN4 spec.
      For NB-IoT RAN4 did not specify scheduling patterns RAN5 was expecting which caused delays
    NR FR1 the UL RMC and OCNG patterns are still missing and not discussed in RAN4 even as indicated in RAN5 LS R5-182094.
Annex A (and some other Annexes) is formative so once anything is missing in RAN4 spec it will bring a direct impact as serious delay for RAN5 core work.

## Slide 3: General idea on how to avoid future delay
RAN4 keeps the responsibility of setting up UE RF/performance requirements
    All the essential parameters (as examples referred to current LTE UE spec 36.101 with all the test parameters specified in Tables in Chapter 6, 7, 8, 9, 10) should be still kept in RAN4 NR UE spec (38.101-1/2/3/4).
    Alignment among companies for RF/performance requirements is kept in RAN4
Some testing related parameters (non-performance critical parameters) can be shifted to RAN5, if the capacity in RAN5 allows, in order to avoid any unnecessary delay for future NR work
    Mainly some Annexes such as RMC and OCNG patterns
    How to decide which parts could be taken over by RAN5 should be based on group discussions by both RAN4 and RAN5. (Joint session is preferred)
      Propose to go through Annex in LTE UE spec 36.101 as example for NR work.
      Following slides bring an initial thought on how to split the work of Annex by taking LTE UE spec 36.101 as example

## Slide 4: Annex A in 36.101 (Detailed parameters moved to RAN5?)
A.1 General
A.2 UL RMC
A.3 DL RMC
A.4 CSI RMC
A.5 OCNG patterns
A.6 Sidelink RMC
A.7 Sidelink reference resource pool config
A.8 V2X RMC
A.9 V2X reference resource pool config

## Slide 5: Annex B in 36.101(Kept in RAN4)
B.1 Static channel
B.2 Multi-path fading channel
  MIMO channel models
B.3 HST channel
B.4 Beamforming model
B.5 Interference model for Type A receiver
B.6 Interference model for Type B receiver
B.7 Interference model for Control channel Type A and Type B receiver
B.8 Burst transmission models for LAA

## Slide 6: Annex C-E in 36.101
C: Downlink Physical Channels (Detailed parameters moved to RAN5?)
  C.1 General
  C.2 Set-up
  C.3 Connection
    Measurement of performance requirement (Power allocation)
D: Characteristics of the interfering signal (Kept in RAN4 but moved to the other parts (core test parts or subclause in Annex B) instead of one standalone chapter as Annex D)
  D.1 General
  D.2 Interference signals
E: Environmental conditions (Kept RAN4)
  E.1 General
  E.2 Environmental
    E.2.1 Temperature
    E.2.2 Voltage
    E.2.3 Vibration (To be removed? since it’s not tested in RAN5)

## Slide 7: Annex F-H in 36.101
F: Transmit modulation (Kept in RAN4)
  F.1 Measurement Point
  F.2 Basic Error Vector Magnitude measurement
  F.3 Basic in-band emissions measurement
  F.4 Modified signal under test
  F.5 Window length
  F.6 Averaged EVM
  F.7 Spectrum Flatness
G: Reference sensitivity level in lower SNR (Informative. To be removed in NR spec?)
H: Modified MPR behaviour (Kept in RAN4 but to be discussed how to specify it for NR?)

## Slide 8: Challenge for NR spec 38.101-1/2/3/4 Annex
UE RF and Perf have separated spec for 38.101 so we can’t really keep the same Annex index as LTE in any case
Any common parts e.g. channel models, interference models, test models between UE RF and performance should be duplicated in the Annexes in all 38.101-1/2/3/4, regardless Annex A (RMC and OCNG) ends in RAN4 or RAN5 specs.

## Slide 9: Way forward
RAN4/RAN5 discuss the possibility of moving the responsibility of parts of Annex of 38.101 (e.g. RMC and OCNG) to RAN5, with the intention to avoid delay in RAN5 for future NR work, as proposed in Page 3 joint session is preferred.
    In practice if possible, RAN4 will decide targeted code rate for per slot basis and any other per slot parameters related to deciding the RMC and brings examples on how to define the RMC by proper calculations.

## Slide 10
http://www.3gpp.org/ftp/TSG_RAN/WG4_Radio/TSGR4_87/Docs/R4-1806121.zip