## Slide 1: WF on measurement gaps for dense PRS
Ericsson
3GPP TSG-RAN WG4 Meeting #87 R4-1806195
Busan, Republic of Korea, 21st – 25th May 2018
Agenda Item: 6.20.4.4

## Slide 2: New gaps and RSTD measurements
The existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps shall also apply with the new gaps
The applicability of the new measurement gap patterns need to be clarified

## Slide 3: New and legacy measurement gap patterns
Option 1 [R4-1805955] applies: using the earlier configured leagacy gaps shall be suspended during the RSTD measurement period (while new gaps are used) and resumed after the RSTD measurements are complete (when new gaps are no longer used)
The new measurement gaps shall be stopped upon completing the RSTD measurements

## Slide 4: New gaps and RRM/RLM measurements
Impact on RRM requirements:
  It is clarified in TS 36.133 that the measurement period may be longer for RRM measurements if during the measurement period the UE is configured with one of the new measurement gap patterns for RSTD measurements
RLM requirements:
  The existing RLM requirements for UE Cat M1 and Cat M2 can be met when there is no overlap between the new measurement gaps and MPDCCH subframes configured for UE monitoring

## Slide 5: New measurement gap patterns
Gap Pattern Id | MGL (ms) | MGRP (ms) | Applicability
rstd0 | 6 | 40 | Only for CE Mode A
rstd1 | 10 | 80 | 
rstd2 | 10 | 160 | 
rstd3 | 10 | 320 | 
rstd4 | 10 | 640 | 
rstd5 | 10 | 1280 | 
rstd6 | 14 | 160 | 
rstd7 | 14 | 320 | 
rstd8 | 14 | 640 | 
rstd9 | 14 | 1280 | 
rstd10 | 32 | 320 | Only for CE Mode B
rstd11 | 32 | 640 | Only for CE Mode B
rstd12 | 32 | 1280 | Only for CE Mode B
rstd13 | 54 | 640 | Only for TDD with CE Mode B
rstd14 | 54 | 1280 | Only for TDD with CE Mode B
rstd15 | 64 | 640 | Only for measuring a cell based on two PRS configurations
rstd16 | 64 | 1280 | Only for measuring a cell based on two PRS configurations
rstd17 | 80 | 640 | Only for measuring a cell based on three PRS configurations
rstd18 | 80 | 1280 | Only for measuring a cell based on three PRS configurations
NOTE 1: Gap patterns rstd0-rstd18 can only be used during the corresponding RSTD measurement period and only for measuring on the carrier frequencies for which the UE is configured via LPP [24] to perform RSTD measurements requiring gaps. |  |  |