## Slide 1: Way forward on RRM measurement accuracy requirements in NR
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.11.1
R4-1807293

## Slide 2: Way forward on RSRP measurement accuracies
Define the RSRP measurement accuracy requirements proposed in Table 1.
Table 1: Summary on RSRP Measurement Accuracy Requirements in NR
Measurement Case | RS Type | Measurement Quantity | Absolute/Relative Accuracy | Requirements | Margin type
Intra-frequency RSRP | SSB based | SS-RSRP | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | Only baseband
 |  | L1-RSRP for beam recovery | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Not define | N/A
 |  | L1-RSRP for beam reporting | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | Only baseband
 | CSI-RS based | CSI-RSRP | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | Only baseband
 |  | L1-RSRP for beam recovery | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Not define | N/A
 |  | L1-RSRP for beam reporting | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | Only baseband
Inter-frequency RSRP | SSB based | SS-RSRP | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | baseband + RF
 | CSI-RS based | CSI-RSRP | Absolute Accuracy | Define | baseband + RF
 |  |  | Relative Accuracy | Define | baseband + RF

## Slide 3: Way forward on RSRPQ/SINR measurement accuracies
Define the RSRQ/SINR measurement accuracy requirements proposed in Table 2.
Table 2: Summary on RSRQ/SINR Measurement Accuracy Requirements in NR
Measurement Case | RS Type | Measurement Quantity | Absolute/Relative Accuracy | Requirements | Margin type
Intra-frequency RSRQ | SSB based | SS-RSRQ | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Not define | N/A
 | CSI-RS based | CSI-RSRQ | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Not define | N/A
Inter-frequency RSRQ | SSB based | SS-RSRQ | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Define | baseband + RF
 | CSI-RS based | CSI-RSRQ | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Define | baseband + RF
Intra-frequency SINR | SSB based | SS-SINR | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Not define | N/A
 | CSI-RS based | CSI-SINR | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Not define | N/A
Inter-frequency SINR | SSB based | SS-SINR | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Define | baseband + RF
 | CSI-RS based | CSI-SINR | Absolute Accuracy | Define | Only baseband
 |  |  | Relative Accuracy | Define | baseband + RF

## Slide 4: Way forward on NR measurement accuracy requirements
The measurement accuracy requirements shall be separately defined for FR1 and FR2 in considering that RF margin can be different.
RAN4 investigate the RF margin assumed for each measurement quantity, including RSRP measurement, RSRQ measurement, and SINR measurement.
The SINR side condition of SS-RSRP/RSRQ/SINR accuracy requirements can be defined as SINR≥-6dB.