## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan, Korea(Republic of), 21 - 25 May 2018
Huawei,HiSilicon
Way forward on UE FeNB-IoT TDD demodulation performance
R4-1807900

## Slide 2: FeNB-IoT TDD
NPBCH
  Reuse the NPBCH FDD performance requirements for NPBCH TDD, but with RMC and test parameters updates for TDD
NPDSCH
  Not define performance requirements for the scenarios with the special subframe configuration 0 and 5 that the number of OFDM symbols in DwPTS equals to 3
  Select special subframe configuration #4 for the scenario that the number of OFDM symbols in DwPTS is larger than 3 for the related NPDSCH TDD demodulation performance evaluation.
    Consider to add a certain margin [0.5]dB on top of the existing NPDCH FDD performance requirements
NPDCCH
    Adopt the similar approach as NPDSCH TDD for NPDCCH TDD demodulation performance requirements evaluation.