## Slide 1: Wayforward on BWP switching
Mediatek
3GPP TSG-RAN WG4 RAN#87
Busan, South Korea, 21 – 25 May, 2018
R4-1808001
Document for: Approval

## Slide 2: Background
RAN4 sent an LS R4-1702029 to RAN1 on the RF switching time in Feb 2017
RAN4 sent an LS R4-1803283 to RAN1 and RAN2 on the BWP switching delay
  the numbers in the table are calculated from the end of the last symbol including the DCI indicating the BWP switch and until BB processing delay and RF transition time has been completed
RAN1 sent an LS R4-1806106, expecting requirement for the BWP switching delay will be specified in RAN4 spec
RAN4 agreed an WF R4-1805540 on aspects to be considered in interruption requirement due to BWP switching
In TS38.331(15.1.0) BWP configurations include also baseband parameters. BWP switching could involve only baseband parameter changes.
In RAN1#91, RAN1 agreed that interruption on the cell with BWP switching equals the whole transition time (see Annex A)

## Slide 3: Wayforward - General
In the RAN4# 88 meeting, companies are encouraged to check the agreements listed in background page and consolidate the common RAN4 understanding on following time units
  Transition time of BWP switch (In RAN1 agreement in Annex A)
  BWP switching delay (in RAN4 reply LS R4-1803283)
  Interruption duration due to BWP switching (in RAN4 WF 4-1805540)
  and how the corresponding UE actions are concluded in above time unites, e.g.,
  DCI decoding
  RF/BB parameter calculating and loading
  Applying the new parameters
Depending on the conclusions, RAN4 identifies if any update of the RAN1/RAN4 agreement is needed
Figure for information: time line of BWP-switching CC
DCI decoding
End of the control symbol carrying DCI switching command
RF/BB parameter calculating and loading
Applying the new parameters
Start of the new BWP

## Slide 4: Wayforward - Delay
Agreement during online session
  BWP switch delay requirement is specified in the unit of slot of the serving cell, if the requirement is defined
  The reference SCS when SCS changes from SCS1 to SCS2 is the lager SCS
FFS whether to allow additional BWP switching delay for UE channel estimation
Determine in the next meeting the BWP switching delay when only baseband parameters (including DL and UL) are involved
  Option 1: Same as the delay needed for the BWP switching with RF re-tuning
  Option 2: Same as the delay needed for the BWP switching with SCS change only

## Slide 5: Wayforward - Interruption
Interruption occurs other serving cells for scenarios 1, 2, 3
  FFS whether interruption can be avoided for those serving cells in different FR to the BWP-switching cell, if UE claimed the supporting of per-FR gap
  FFS the interruption duration
    Option A: the same switching delay.
    Option B: re-use the conclusion in Scell activation
    Option C: other values
FFS whether Interruption occurs for scenario 4 and if so, what the victim cells are.
FFS whether any baseband parameters in the BWP configuration in TS38.331 will cause interruption and if so, what the victim cells are.

## Slide 6: Annex A: RAN1 agreement in RAN1#91 for information
Agreements:
  A UE is not expected to receive DL signals or transmit UL signals during the transition time of active DL or UL BWP switch
    For DCI-based active BWP switch, from RAN1 perspective, the transition time of active DL or UL BWP switch is the time duration from the end of last OFDM symbol of the PDCCH carrying the active BWP switch DCI till the beginning of a slot indicated by K0 in the active DL BWP switch DCI or K2 in the active UL BWP switch DCI
    For timer-based active BWP switch, from RAN1 perspective, the transition time of active DL or UL BWP switch is the time duration from the beginning of the subframe (FR1) or from the beginning of the half-subframe (FR2) immediately after a BWP timer expires till the beginning of a slot UE is able to receive DL signals or transmit UL signals in the default DL BWP for paired spectrum or the default DL or UL BWP for unpaired spectrum