## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan, Korea(Republic of), 21 - 25 May 2018
Huawei, Ericsson, Nokia, Nokia Shanghai Bell, Samsung
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1808025

## Slide 2: PUCCH Requirements
Format:
  Requirements will be defined for PUCCH format 0/1/2/3
  FFS PUCCH format 4.
  The applicability for each format are based on BS declaration

## Slide 3: Test setup
Test metric
  PF0/1
    DTX to Ack
    Missed Ack
  PF2/3/4: FFS
Modulation
  QPSK is tested
  FFS π/2-BPSK for PF3/4
FFS multi-slot PUCCH
Hopping
  Frequency hopping: enable
  Group and sequence hopping: disable

## Slide 4: Simulation assumption for format 0
Number of bits: 1bit
Number of OFDM symbols
  1 OFDM symbol
  2 OFDM symbols not precluded
Metric
  DTX to ack
  Missed Ack

## Slide 5: Simulation assumption for format 1
Number of bits: 2 bits
Number of OFDM symbols
  [14] OFDM symbols
  Other options not precluded
Metric
  DTX to ack
  Missed Ack

## Slide 6: Simulation assumption for format 2
Number of bits:
  Option 1: [4] bits,
  Other options are not precluded
Number of OFDM symbols
  1 and/or 2 OFDM symbols
  Other options are not precluded
Number of PRBs:
  Option 1: [8]
  Other options are not precluded

## Slide 7: Simulation assumption for format 3
Number of bits:
  Option 1: [16 bits]
  Other options are not precluded
Number of OFDM symbols
  [14] OFDM symbol
  Other options are not precluded
Number of PRBs
  Option 1: [1] PRB
  Other options are not precluded
DMRS pattern
  Option 1: No additional DMRS, and/or
  Option 2: additional DMRS