## Slide 1: WF on idle UE behavior for HPUE
NTT DOCOMO
RAN4#87, Busan, Korea R4-1808181

## Slide 2: Background:
In LTE, power class 3 (PC3) is default power class, and high power capable UE (e.g. PC2) assumes 23dBm of output power at maximum if eNB does not signal Pmax > 23dBm except for band 41[TS36.101]
If similar approach is applied for NR, there is a problem for cell measurement criterion for HPUE in idle mode
  See slide #3 and #4 for details
  Note: TS36.304 is the RAN2 specification for cell selection criterion
Note: Assumption of deployment scenario:
  Both PC2 and PC3 are in the network
  Cell coverage is well planed for PC3 UE to keep a connectivity to the network
TS36.101-1, Sect. 6.2.2
For each supported frequency band other than Band 41, the UE shall:
- if the UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the band is a TDD band whose frame configuration is 0 or 6; or
- if the IE P-Max as defined in TS 36.331 [7] is not provided; or
- if the IE P-Max as defined in TS 36.331 [7] is provided and set to the maximum output power of the default power class or lower;
- meet all requirements for the default power class of the operating band in which the UE is operating and set its configured transmitted power as specified in sub-clause 6.2.5;
- else (i.e the IE P-Max as defined in TS 36.331 [7] is provided and set to the higher value than the maximum output power of the default power class):
- meet all requirements for the supported power class and set its configured transmitted power class as specified in sub-clause 6.2.5;

## Slide 3: Problem statement (1/2)
 | PC2 | PC3
Qrxlevmeas | -125 | -125
Qrxlevmin | -124 | -124
Pcompensation | 0 | 3
Srxlev | -1 | -4
Assumption
P-Max = 26 is broadcasted
Cell selection criterion（Qrxlevminoffset and Qoffsettemp are zero for simplicity）
  Srxlev = Qrxlevmeans (RSRP) – Qrxlevmin - Pcompensation
Qrxlevmin = -124dBm is broadcasted (assuming cell edge of PC3 is -124dBm)
SIntraSearchP = 0dBm
 | PC2 | PC3
Qrxlevmeas | -122 | -122
Qrxlevmin | -124 | -124
Pcompensation | 0 | 3
Srxlev | 2 | -1
PC3 UE needs to perform unnecessary intra-frequency measurement
BS＃2
RSRP < -124dBm
RSRP < -127dBm
Serving cell
Neighbor cell
BS＃1

## Slide 4: Problem statement (2/2)
 | PC2 | PC3
Qrxlevmeas | -125 | -125
Qrxlevmin | -127 | -127
Pcompensation | 0 | 3
Srxlev | 2 | -1
Assumption
P-Max = 26 is broadcasted
Cell selection criterion（Qrxlevminoffset and Qoffsettemp are zero for simplicity）
  Srxlev = Qrxlevmeans (RSRP) – Qrxlevmin - Pcompensation
Qrxlevmin = -127dBm is broadcasted (assuming cell edge of PC3 is -124dBm)
SIntraSearchP = 0dB
 | PC2 | PC3
Qrxlevmeas | -122 | -122
Qrxlevmin | -127 | -127
Pcompensation | 0 | 3
Srxlev | 5 | 2
PC2 UE may not perform intra-frequency measurement for BS#2 even if BS#2 is optimal
BS＃2
RSRP < -124dBm
RSRP < -127dBm
Serving cell
Neighbor cell
BS＃1

## Slide 5: Proposal
Potential solutions:
  Alt.1: Resolve this issue in RAN2 under the assumption that HPUE shall assume 23dBm of output power (i.e. default power class) at maximum if gNB does NOT signal any Pmax value to HPUE
  Alt.2: PC2 UE can assume 26dBm of output power at maximum if gNB does NOT signal any Pmax value to HPUE at least for band n41, n77, n78 and n79
Send to RAN2 to ask to resolve the cell selection issue in idle mode
Final decision shall be made by RAN4 #88 (in Aug.) considering RAN2 progress
  Note: The current description in the Sect. 6.2.2 of TS38.101-1 is not final decision in RAN4

## Slide 6: Annex: Cell selection criterion (TS36.304)

## Slide 7: Annex : Measurement rules for cell re-selection (TS36.304, Sect. 5.2.4.2)
Following rules are used by the UE to limit needed measurements:
If the serving cell fulfils Srxlev > SIntraSearchP and Squal > SIntraSearchQ, the UE may choose not to perform intra-frequency measurements.
Otherwise, the UE shall perform intra-frequency measurements.
The UE shall apply the following rules for E-UTRAN inter-frequencies and inter-RAT frequencies which are indicated in system information and for which the UE has priority provided as defined in 5.2.4.1:
For an E-UTRAN inter-frequency or inter-RAT frequency with a reselection priority higher than the reselection priority of the current E-UTRA frequency the UE shall perform measurements of higher priority E-UTRAN inter-frequency or inter-RAT frequencies according to [10].
For an E-UTRAN inter-frequency with an equal or lower reselection priority than the reselection priority of the current E-UTRA frequency and for inter-RAT frequency with lower reselection priority than the reselection priority of the current E-UTRAN frequency:
- If the serving cell fulfils Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, the UE may choose not to perform measurements of E-UTRAN inter-frequencies or inter-RAT frequency cells of equal or lower priority unless the UE is triggered to measure an E-UTRAN inter-frequency which is configured with redistributionInterFreqInfo.
- Otherwise, the UE shall perform measurements of E-UTRAN inter-frequencies or inter-RAT frequency cells of equal or lower priority according to [10].
- If the UE supports relaxed monitoring and s-SearchDeltaP is present in SystemInformationBlockType3, the UE may further limit the needed measurements, as specified in sub-clause 5.2.4.12.