## Slide 1: 3GPP TSG RAN WG4 Meeting #87 R4-1808189 Busan, Korea, May 21st – 25th, 2018
WF on spherical coverage requirement on FR2
Qualcomm Incorporated, Verizon, Telstra, NTT Docomo, CMCC, Vodafone, Orange, Telecom Italia, AT&T, Motorola Mobility, Nokia, Nokia Shanghai Bell, China Telecom, China Unicom, BT plc., Ericsson, Dish Networks, SKT, KT, Softbank, Deutsche Telekom, Interdigital, T-Mobile USA, NXP, US Cellular, Panasonic, SGS Wireless, Bureau Veritas,

## Slide 2: Background
The impact of spherical coverage on the network performance shows that better spherical coverage leads to better system performance and network coverage as shown in R4-1807658

## Slide 3: Way forward on spherical coverage requirements
24-28GHz bands
  50%-ile cdf of spherical coverage requirement for EIRP for handheld UE is defined as 12.5dBm (9.9dB lower than peak EIRP)
  50%-ile cdf of spherical coverage requirement for EIS for handheld UE is defined as -78.4dBm for 50MHz SC QPSK 1/3 (9.9dB higher than EIS)
39GHz bands
  50%-ile cdf of spherical coverage requirement for EIRP for handheld UE is defined as 8.5dBm (12.1dB lower than peak EIRP)
  50%-ile cdf of spherical coverage requirement for EIS for handheld UE for GHz is defined -73.6dBm for 50MHz SC QPSK 1/3 (12.1dB higher than peak EIS)