## Slide 1: WF on the clarification of NR BS TAE applicable scenarios
NTT DOCOMO, INC.
R4-1808289
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 - 25 May, 2018
Agenda 7.7.2.4.2.3

## Slide 2: Background
In RAN4 #86bis, following contribution triggers the discussion of understanding regarding TAE requirements for MIMO or TX diversity, and intra-band C CA.
  R4-1805339 NR BS TAE for distributed MIMO deployment scenarios NTT DOCOMO, INC.
In RAN4 #86bis, following WF was agreed.
  R4-1805804 WF on NR BS TAE for inter-BS NTT DOCOMO, INC.
In RAN4 #87, this issue is further discussed based on following contributions.
  R4-1807576 NR BS TAE for inter-BS cases, NTT DOCOMO, INC
  R4-1806400 Discussion on scenario for BS TAE, Samsung
  R4-1807878 On NR BS TAE requirement for inter-BS, Nokia, Nokia Shanghai Bell
  R4-1807190 NR BS TAE for inter-BS scenario, NEC
  R4-1807182 Input to WF on NR BS TAE for inter-BS for MIMO, TX diversity and continuous CA, Ericsson LM R4-1807183 Input to WF on NR BS TAE for inter-BS with respect to inter-band CA and non-contiguous CA, Ericsson LMBackground can be found in above document.
This document summarizes the Agreements/WF on NR BS TAE requirement

## Slide 3: Agreements(1/2)
For MIMO or Tx diversity, or intra-band contiguous CA case
For conducted requirment
  The current TAE requirement is applicable between any connectors sharing the same oscillator.
For radiated requirement
  The current TAE requirement is applicable between different signals transmitted from the same oscillator.
Whether specify TAE requirement, which is applicable between any connectors not sharing oscillator, or not is FFS, and continue discussion in If specify, the required value is FFS.
Companies are encouraged to provide views whether specify TAE requirement which is applicable between any connectors not sharing oscillator, or not.
Configurations | TAE requirement | 
 | For conducted requirement, between connectors sharing an oscillator For radiated requirement, between different signals generated by an oscillator | For conducted reuirement, between connectors not sharing the oscillator For radiated requirement, between different signals transmitted from the different oscillator
MIMO or Tx div. | 65ns | FFS in Rel-16
intra-band C CA | 260ns (FR1), 130ns (FR2) | 

## Slide 4: Agreements(2/2)
For intra-band non-contiguous CA or inter-band CA case
For conducted requirement
  The current TAE requirement is applicable between any connectors regardless of whether sharing oscillator or not
For radiated requirement
  The current TAE requirement is applicable between different signals regardless of whether sharing oscillator or not
Configurations | TAE requirement | 
 | For conducted requirement, between connectors sharing the same oscillator For radiated requirement, between different signals transmitted from the same oscillator | For conducted reuirement, between connectors not sharing the oscillator For radiated requirement, between different signals transmitted from the different oscillator
intra-band NC CA | 3us | 3us
inter-band CA | 3us | 3us