## Slide 1: WF on FR2 DL 256QAM
NTT DOCOMO, INC., Nokia, Huawei Deutsche Telekom, BT plc, AT&T, KDDI, Orange, T-Mobile, KT, CMCC, Verizon, C Spire, SK Telecom
R4-1808506
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 - 25 May, 2018
Agenda 7.1.1

## Slide 2: Background
Companies | Detailed proposals
Intel (R4-1806296) | Do not introduce 256QAM DL/UL performance requirements for FR2 in Rel-15.
CATT(R4-1806715) | RAN4 focus up to 64QAM modulation scheme for FR2 in Rel-15 and consider 256QAM in later releases.
Ericsson, Intel, CATT, Samsung, MediaTek, Sony (R4-1807448) | Evaluation of 256QAM should be considered for release 16 No requirements for 256QAM in FR2 are defined in release 15
China Telecom (R4-1806823) | Define DL 256QAM for FR2 as an optional feature in Rel-15. Set new WID for DL 256QAM for FR2 to work on the total requirements for BS and UE.
Huawei (R4-1807520) | Define the DL 256QAM for FR2 as an optional feature in Rel-15. The EVM requirement in Table 2-2 is (3.5% for 256QAM) specified for FR2 BS.
NTT DoCoMo (R4-1807573) | In Rel-15, introduce 256QAM BS Tx EVM requirement in core spec 38.104. Required 256QAM EVM value for NR FR2 BS is [3.5]%.
Nokia (R4-1807874) | Include 256QAM in NR Rel-15 FR2 specification as a manufacturer’s declaration based requirement and reuse FR1 DL Tx EVM requirements.
In RAN4 #87, DL 256 QAM is discussed in following contributions.
In this contribution, the agreements are summarized.

## Slide 3: Agreement
Define DL 256QAM for FR2 as an optional feature in Rel-15.
Only specify 256QAM BS Tx EVM requirement for FR2 in core spec 38.104 in Rel-15, and the required EVM value is 3.5%.
  Considering concerns about power back off and cell coverage issues, the requirement is introduced for Medium Range and Local Area BS in Rel-15.(Not introduce 256QAM BS Tx EVM for Wide Area BS in Rel-15)
    FFS for Wide Area BS
  Considering concerns about EVM balancing between BS and UE requirements, the value 3.5% willmay be reconsidered/revisited in later Release based on the detail analysis in RAN4. if needed.
  Add the following NOTE in TS 38.104.
    NOTE: The 256QAM EVM value will be reconsidered/revisited in later Release.
Not define UE Rx requirements (RF and/or perf) for FR2 256QAM in Rel-15.
  Rel-15 UE doesn't need to support DL256QAM
  FFS how to introduce 256QAM related UE Rx requirements (RF and/or perf) in later release.
A potential new WID for DL 256QAM for FR2 to complete remaining requirements for BS and UE in Rel-16 can be discussed in RAN plenary. It is up to RAN plenary to approve the new WID.