## Slide 1: Proposed conclusion on BS requirements for LTE-NR uplink sharing
Huawei, HiSilicon, Vodafone, Orange, Intel, China Telecomm, Telefonica, CMCC, KDDI, BT plc, MediaTek, Deutsche Telekom, Spreadtrum
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21-24 May, 2018
Agenda: 7.3.2
R4-1808398

## Slide 2: Background
RAN4 has been discussing BS requirements for UL sharing for several meetings
At RAN4_AH-1801, it was agreed to focus on two scenarios:
  Scenario 1: LTE and NR subcarriers with same SCS (15kHz) and NR has 7.5kHz raster shift in Rel-15
    LTE and NR with different waveforms (CP-OFDM and S-OFDM) and waveform conforming technique
  Scenario 2: LTE and NR subcarriers with different SCS
    LTE and NR with different waveforms (CP-OFDM and S-OFDM) and waveform conforming technique

## Slide 3: Background
For Scenario 1, the following aspects were investigated [R4-1801568, R4-1803893, R4-1808397]:
  Orthogonality and guard band for the cases of both perfect and realistic time and frequency synchronization between different UEs
  RX requirements with TX on
  Potential RX requirements differentiation between UL sharing from network perspective and UE perspective
For Scenario 2, the following aspects were investigated [R4-1800920]:
  Orthogonality and guard band

## Slide 4: Proposed conclusion
It is proposed that for UL sharing from network perspective or UL sharing from UE perspective with TDM operation, no additional NR BS RF requirements need to be introduced for scenario 1 with the target BLER larger than 1% (without the use of HARQ).
  FFS if additional BS demodulation requirements are needed
  FFS if additional BS requirements are needed for UL sharing from UE perspective with FDM operation
FFS if additional NR BS requirements need to be introduced for scenario 2