## Slide 1: WF for A-MPR and MSD of DC_3A_n3A CHTTL
3GPP TSG-RAN WG4 Meeting #88 R4-1810375 Gothenburg, SE, 20th – 24th August, 2018

## Slide 2: Backgrounds
DC_3A_n3A is introduced in Rel.15 with single UL switched support
It is agreed to continue studying dual uplink transmission mode for DC_3A_n3A in Rel.16
In the previous RAN4 meetings, several agreements related to the intra-band EN-DC were agreed for specific bands only

## Slide 3: Proposals
Define A-MPR and MSD for dual uplink support for DC_3A_n3A
  A-MPR and MSD should be defined for a reference architecture of 2PA with 2 antennas
    4 dB post-PA insertion loss on each Tx chain
    10 dB antenna isolation
  A-MPR
    A-MPR is used to address IM3 impact on general spectrum mask and ACLR overlap
    At least A-MPR will be defined for Type 1 and Type 2 UEs
  MSD
    At least one MSD test point for the 3rd IMD falling into the 1st CC from the lower edge of Band 3/n3 is needed

## Slide 4: Referense
  [1] R4-1810372, “Initial analysis for A-MPR and MSD for dual uplink transmission of DC_3_n3”, CHTTL, RAN4#88
  [2] R4-1805761, “WF for UE RF AH specific for DC_(n)71B”, Nokia, RAN4#86bis
  [3] R4-1805774, “WF on B41/n41 intra-band EN-DC requirements”, SPRINT Corporation, RAN4#86bis