## Slide 1: Way forward on new gaps for dense PRS configuration
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, 20th – 24th August, 2018
Agenda item: 6.5.4.1
R4-1810630

## Slide 2: Background in R4-1808476
RSTD measurement period:
  The existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps shall also apply with the new gaps
RLM requirements:
  When the UE is configured with new measurement gaps for RSTD measurements, the UE shall also perform RLM. If there is no overlap between the new measurement gaps and configured MPDCCH subframes for UE monitoring, the UE shall meet the existing requirements; otherwise, the out-of-sync and in-sync evaluation periods can be longer than currently defined in 36.133
RRM requirements:
  RRM cell identification delay and measurement delay may be longer while the UE is using a new measurement gap pattern configured for RSTD measurements
RAN4 to further discuss whether Note 1 after Table 8.1.2.1-2 needs to be updated due to the introduction of the new measurement gaps

## Slide 3: WF
Define applicability for the dense PRS gap patterns under certain principles,
  Dense PRS gap patterns are not used for RRM measurements
  Dense PRS gap patterns are not used for RSTD measurements without dense PRS configuration
  Patterns designed for TDD are not used for FDD mode, which are rstd9 ~ rstd 11, rstd 15 and rstd 16
  Discuss how to define the applicability to better align with the PRS configuration
Upon receiving RSTD measurement configuration, UE requests the proper RSTD gap pattern from the serving eNB.
Upon receiving RSTD measurement configuration with new gaps, UE should follow enhanced RRM requirements.
Clarify the applicability of RLM requirements for the cases in which the dense PRS gaps are configured.

## Slide 4: Gap pattern applicability
Gap Pattern Id | Measurement Gap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) | Applicability
rstd0 | 10 | 80 | TBD
rstd1 | 10 | 160 | TBD
rstd2 | 10 | 320 | TBD
rstd3 | 10 | 640 | TBD
rstd4 | 10 | 1280 | TBD
rstd5 | 14 | 160 | TBD
rstd6 | 14 | 320 | TBD
rstd7 | 14 | 640 | TBD
rstd8 | 14 | 1280 | TBD
rstd9 | 24 | 320 | TDD only
rstd10 | 24 | 640 | TDD only
rstd11 | 24 | 1280 | TDD only
rstd12 | 32 | 320 | TBD
rstd13 | 32 | 640 | TBD
rstd14 | 32 | 1280 | TBD
rstd15 | 54 | 640 | TDD only
rstd16 | 54 | 1280 | TDD only
rstd17 | 64 | 640 | CE mode B only
rstd18 | 64 | 1280 | CE mode B only
rstd19 | 80 | 640 | Cat M1 CE mode B only
rstd20 | 80 | 1280 | Cat M1 CE mode B only
NOTE 1: Measurement gap patterns rstd0─rstd20 can only be configured for RSTD measurements requiring such gaps and used during the RSTD measurement period corresponding to these measurements. |  |  |