## Slide 1: Way forward on eFeMTC UE demodulation and CSI
Ericsson
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 – 24 August, 2018
R4-1811372

## Slide 2: Way forward for PDSCH for BL/CE UEs
DL 64QAM
  CE Mode A with 3PRB allocation, TBS=968 and under EPA5 2x1 low
  Transmission mode: TM2
High speed scenario:
  TM2, QPSK 1/3, (TBS=504bits with 6PRB), EPA200, 2x1 Low, CE Mode A, without frequency hopping
  No Repetition
CRS muting
  Select test cases from
    Cat-M1
      8.11.1.1.3.1 Tests 2 (TM2, 16QAM 1/2, 3PRB, CE Mode A, No repetitions)
    Cat-M2
      8.11.1.1.3.2 Tests 2 (TM2, QPSK 1/10, 18PRB, CE Mode B, 32 repetitions)

## Slide 3: Way forward for CQI definition test for CQI table 5 for BL/CE UEs
Companies are encouraged to provide the simulation results to set the SNR test points corresponding to 64QAM
CQI2MCS is given as follows as example:
  Companies are encouraged to verify this table.
  Other options are not precluded.
PRB | Available REs | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
1 | 126 | DTX | 0 | 0 | 0 | 1 | 4 | 5 | 8 | 12 | 14 | 16 | 18 | 21 | 23 | 25 | 27

## Slide 4: Way forward for CQI definition test for CQI table 6 for BL/CE UEs
Companies are encouraged to provide the simulation results to set the SNR test points corresponding to 16QAM
CQI2MCS is given as follows as example:
  Companies are encouraged to verify the options.
  Other options are not precluded.
Option | PRB | Available Res | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
1 | 3 | 378 | DTX | 0 | 2 | 3 | 2 | 1 | 3 | 7 | 9 | 12 | 15 | 16 | 16 | 22 | 25 | 27
2 | 3 | 378 | DTX | 0 | 1 | 2 | 1 | 1 | 2 | 6 | 9 | 12 | 14 | 16 | 16 | 21 | 24 | 27

## Slide 5: Applicability for non-BL CE UEs
FFS: Applicability of the new Rel-15 requirements to non-BL CE UEs.