## Slide 1: WF on data SCS restriction of BWP based on UE CC BW
Qualcomm
RAN4#88, Gothenburg, Sweden R4-1811543

## Slide 2: Background
In RAN4#AH-1801 [1] we agreed to the following
UE behavior
  The UE meets RF requirements related to it’s configured BWP according to UE CBW (no additional BWP related RF requirements)
    FFS whether UE CBW next highest value after BWP bandwidth
  How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
UE RF requirements
  Single BWP case: single CC RF requirements apply with UE CC BW
  Multiple BWPs case : intra-band CA RF requirements apply with UE CC BW
[1] R4-1801006, WF on wideband operation of NR UE, 3GPP TSG-RAN WG4 #AH-1801 Meeting, San Diego, California, USA, Jan. 22 – 26, 2018

## Slide 3: RF requirements for BWP
RF requirements
  Agreement: RF requirements are based on UE CC BW
  RAN2 signaling is configuring UE with multiple CC BW’s (per SCS)
    For a BWP that lies in multiple configured CC BW’s RAN4 needs to decide which RF requirements should apply
    Example in figure: For BWP1 would requirements for CCBW1 or CCBW2 apply

## Slide 4: Proposals for multiple UE CC BW
Current RAN2 signaling allows for SCS specific UE BW’s
Companies to investigate the implication of a UE configured with different UE CC BW’s on BWP switching and RF requirements
Options
  Option 1: Have a “reference” CC BW that is used to determine RF settings
  Option 2: Restrict the max configured UE CC BW based on the smallest SCS configured
    If UE is being configured with CC BW’s for both 15 kHz and 30 kHz SCS, the maximum CC BW can be 50 MHz
  Option 3: Maximum configured BWP bandwidth should be SCS specific
  Other options not precluded

## Slide 5: Baseband Limitation
The RF BW that UE chooses for a particular BWP is implementation dependent
  It is up to the UE to operate in either BWP BW or CC BW
  A BWP switch shouldn’t change the RF requirements for the UE
For a UE that chooses to always operate in CC BW
  There are baseband restrictions based on FFT size
  Example:
    UE has FFT size of 4096 (4K ) point
    Consider the scenario where CC BW = 100 MHz, SCS= 30kHz, BWP BW = 50MHz, BWP SCS = 15kHz
    The UE in the above scenario would need a 8K point FFT which violates its capability
  Need SCS restriction in BWP based on UE CC BW
Two options to resolve this
  Option 1: SCS restriction needs to be across UE’s
  Option 2: Define a UE capability for UE’s that will not need this restriction.