## Slide 1: Tx/Rx TRP spurious emissions
Huawei
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20th – 24th Aug 2018
R4-1811672

## Slide 2: Back ground
The following slide contains a summary of the contribution on the MU and TT values for the TRP spurious emissions requirements

## Slide 3
Requirement |  | Unit | Conducted MU |  |  | Conducted TT |  |  | OTA MU |  |  |  |  |  |  |  |  |  |  |  |  |  |  | OTA TT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Name | WF ref |  | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  |  | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  | 
 | c |  | AAS | AAS | E-UTRA | AAS | AAS | E-UTRA | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  | 
Company | c |  |  |  |  |  |  |  | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree
Rx Spurious emssions | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
30 MHz ≤ f ≤ 4 GHz | 4 | dB | 2 |  |  | 0 |  |  | 2.9 | Tx | 1,2 up to 3, 1.4 3-4 |  |  | 2.9 | Tx | 1,2 up to 3, 1.4 3-4 |  |  | x |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.9 | Tx | 0 | 0.0 |  | 2.9 | Tx | 0.0 | 0.0 |  | x |  | 0.0 | 0.0 | 
4 GHz < f ≤ 19 GHz | 4 | dB | 4 |  |  | 0 |  |  | 5.0 | Tx | 1,4 up to 12, 1,6 12-19 |  |  | 5.0 | Tx | 1,4 up to 12, 1,6 12-19 |  |  | x |  | 1,4 up to 12, 1,6 12-19 |  |  | 5.0 | Tx | 0 | 0.0 |  | 5.0 | Tx | 0.0 | 0.0 |  | x |  | 0.0 | 0.0 | 
19 GHz < f ≤ 26 GHz | 4 | dB | x | x | x | x | x | x | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 0 | 0.0 |  | x |  | 0 | 0.0 |  | x |  | 0 | 0.0 | 
Transmitter spurious emissions, Mandatory Requirements | 4 | dB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
30 MHz ≤ f ≤ 4 GHz | 4 |  | 2.0 |  |  | 0 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 
4 GHz < f ≤ 19 GHz | 4 |  | 4.0 |  |  |  |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 
19 GHz < f ≤ 26 GHz | 4 |  | x | x | x |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 
6.7.6.4 Transmitter spurious emissions, Additional spurious emission requirements (3GPP co-existence) | 4 | dB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
> -60dBm, f ≤ 3.0GHz | 4 |  | 2.0 |  |  | 0 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  | 
> -60dBm, 3.0GHz < f ≤ 4.2GHz | 4 |  | 2.5 |  |  |  |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  | 
> -60dBm, 4.2GHz < f ≤ 6.0GHz | 4 |  | 3.0 |  |  |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  | 
> -60dBm, 6.0GHz < f ≤ 26.0GHz | 4 |  | x | x | x |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  | 
≤ -60dBm, f ≤ 3.0GHz | 4 |  | 3.0 |  |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  | 0 |  | 3.4 |  |  | 0 |  | 3.4 |  |  | 0 | 
≤ -60dBm, 3.0GHz < f ≤ 4.2GHz | 4 |  | 3.5 |  |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  | 0 |  | 3.9 |  |  | 0 |  | 3.9 |  |  | 0 | 
≤ -60dBm, 4.2GHz < f ≤ 6.0GHz | 4 |  | 4.0 |  |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  | 
≤ -60dBm, 6.0GHz < f ≤ 26.0GHz | 4 |  | x | x | x |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  | 
Mandatory additional e.g. PHS | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Discussion
2 companies have contributed
  Huawei – value are based on conducted MU plus consideration of OTA chamber and SE
  Ericsson – values have been calculated from scratch considering OTA MU analysis and are lower than conducted MU
Compromise
  We can use the conducted MU as a basic for the conducted part measurement accuracy but not explicitly state that its just the conducted MU.
  Propose the following contributor to describe this:
  Conducted measurement uncertainty – Measurement uncertainty of the RF measurement equipment and the associated RF measurement system including filters, attenuators, limiters etc… as necessary for the appropriate test

## Slide 5: Tx mandatory emissions
Requirement |  | Unit | Conducted MU |  |  | Conducted TT |  |  | OTA MU |  |  |  |  |  |  |  |  |  |  |  |  |  |  | OTA TT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Name | WF ref |  | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  |  | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  | 
 | c |  | AAS | AAS | E-UTRA | AAS | AAS | E-UTRA | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  | 
Company | c |  |  |  |  |  |  |  | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree
30 MHz ≤ f ≤ 4 GHz | 4 |  | 2.0 |  |  | 0 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.7 |  | 1,2 up to 3, 1.4 3-4 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 
4 GHz < f ≤ 19 GHz | 4 |  | 4.0 |  |  |  |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 4.9 |  | 1,4 up to 12, 1,6 12-19 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 
19 GHz < f ≤ 26 GHz | 4 |  | x | x | x |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | 0 |  | 0.0 | 0 |  | 0 |  | 0.0 | 0 |  | x |  | 0 | 0 | 

## Slide 6: Tx mandatory emissions - agreements
Currently 2 ranges
  30 MHz ≤ f ≤ 4 GHz
  4 GHz < f ≤ 19 GHz
The frequency breakpoint is at 4GHz, as we now have wanted frequency bands up to 6GHz (for NR at least), up to 6GHz can be considered in-band in some cases so would be expected to have better MU, it is proposed to change the freq breakpoint to 6GHz as follows:
  30 MHz ≤ f ≤ 6 GHz
  6 GHz < f ≤ 19 GHz

## Slide 7: Tx mandatory emissions - agreements
Wide band chamber analysis, new contributors are:
  Conducted measurement uncertainty – as describe don slide 3
  Measurement antenna variation
  FSPL estimation error
  Uncertainty of the absolute gain of the reference antenna
SE is added RSS at 2σ
Proposal
  30 MHz ≤ f ≤ 6 GHz, MU=2.3dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
UID | Uncertainty source | Uncertainty value |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] | 
 |  | 30MHz<f≤6 GHz | 6GHz<f ≤19GHz |  |  |  | 30MHz<f≤6 GHz | 6GHz<f ≤19GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  | 
1 | Positioning misalignment between the AAS BS and the reference antenna | 0.03 | 0.03 | Rectangular | √3 | 1 | 0.02 | 0.02
2 | Pointing misalignment between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
3 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
4 | Polarization mismatch between the AAS BS and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
5 | Mutual coupling between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
6 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
7 | Conducted measurement uncertainty | 1.02 | 2.04 | Gaussian | 1 | 1 | 1.02 | 2.04
8 | Impedance mismatch in the receiving chain | 0.2 | 0.45 | U-shaped | √2 | 1 | 0.14 | 0.32
9 | Random uncertainty | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | Measurement antenna frequency variation | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | FSPL estimation error | 0 | 0 | Gaussian | 1 | 1 | 0 | 0
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2
Stage 1: Calibration measurement |  |  |  |  |  |  |  | 
10 | Impedance mismatch between the receiving antenna and the network analyzer | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
11 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
12 | Impedance mismatch between the reference antenna and the network analyzer. | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
13 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
14 | Polarization mismatch for reference antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
15 | Mutual coupling between the reference antenna and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
16 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
17 | Uncertainty of the network analyzer | 0.13 | 0.2 | Gaussian | 1 | 1 | 0.13 | 0.2
18 | Influence of the reference antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
19 | Reference antenna feed cable loss measurement uncertainty | 0.06 | 0.06 | Gaussian | 1 | 1 | 0.06 | 0.06
20 | Influence of the receiving antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
21 | Uncertainty of the absolute gain of the reference antenna | 0.5 | 0.5 | Rectangular | √3 | 1 | 0.29 | 0.29
22 | Uncertainty of the absolute gain of the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  | 1.11 | 2.11
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  | 2.18 | 4.13
 | SE |  |  |  |  |  | 0.75 | 0.75
 | MU total |  |  |  |  |  | 2.3 | 4.2

## Slide 8: Rx emissions
Requirement |  | Unit | Conducted MU |  |  | Conducted TT |  |  | OTA MU |  |  |  |  |  |  |  |  |  |  |  |  |  |  | OTA TT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Name | WF ref |  | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  |  | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  | 
 | c |  | AAS | AAS | E-UTRA | AAS | AAS | E-UTRA | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  | 
Company | c |  |  |  |  |  |  |  | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree
Rx Spurious emssions | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
30 MHz ≤ f ≤ 4 GHz | 4 | dB | 2 |  |  | 0 |  |  | 2.9 | Tx | 1,2 up to 3, 1.4 3-4 |  |  | 2.9 | Tx | 1,2 up to 3, 1.4 3-4 |  |  | x |  | 1,2 up to 3, 1.4 3-4 |  |  | 2.9 | Tx | 0 | 0.0 |  | 2.9 | Tx | 0.0 | 0.0 |  | x |  | 0.0 | 0.0 | 
4 GHz < f ≤ 19 GHz | 4 | dB | 4 |  |  | 0 |  |  | 5.0 | Tx | 1,4 up to 12, 1,6 12-19 |  |  | 5.0 | Tx | 1,4 up to 12, 1,6 12-19 |  |  | x |  | 1,4 up to 12, 1,6 12-19 |  |  | 5.0 | Tx | 0 | 0.0 |  | 5.0 | Tx | 0.0 | 0.0 |  | x |  | 0.0 | 0.0 | 
19 GHz < f ≤ 26 GHz | 4 | dB | x | x | x | x | x | x | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 0 | 0.0 |  | x |  | 0 | 0.0 |  | x |  | 0 | 0.0 | 

## Slide 9: Rx emissions
As with Tx the frequency breakpoint is changed to 6GHz:
  30 MHz ≤ f ≤ 6 GHz
  6 GHz < f ≤ 19 GHz
The receiver requirements are at a much lower power level so TRP calculation may be affected by the noise floor of the measurement system, the following definition is proposed:
Measurement system dynamic range uncertainty – uncertainty due to the test requirement being close to the measurement equipment noise floor and the noise floor contributing significantly to the TRP total.

## Slide 10: Rx emissions
Same contributors as Tx SE with addition of :
  Measurement system dynamic range uncertainty
SE is added RSS at 2σ
Proposal
  30 MHz ≤ f ≤ 6 GHz, MU=2.5dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
UID | Uncertainty source | Uncertainty value |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] | 
 |  | 30MHz<f≤4 GHz | 4GHz<f ≤19GHz |  |  |  | 30MHz<f≤4 GHz | 4GHz<f ≤19GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  | 
1 | Positioning misalignment between the AAS BS and the reference antenna | 0.03 | 0.03 | Rectangular | √3 | 1 | 0.02 | 0.02
2 | Pointing misalignment between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
3 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
4 | Polarization mismatch between the AAS BS and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
5 | Mutual coupling between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
6 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
7 | Conducted measurement uncertainty (minus missmatch) | 1 | 1.99 | Gaussian | 1 | 1 | 1 | 1.99
8 | Impedance mismatch in the receiving chain | 0.2 | 0.45 | U-shaped | √2 | 1 | 0.14 | 0.32
9 | Random uncertainty | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | Measurement antenan frequency variation | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | FSPL estimation error | 0 | 0 | Gaussian | 1 | 1 | 0 | 0
 | Measurement system dynamic range uncertainty | 0.51 | 0.51 | Gaussian | 1 | 1 | 0.51 | 0.51
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2
Stage 1: Calibration measurement |  |  |  |  |  |  |  | 
10 | Impedance mismatch between the receiving antenna and the network analyzer | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
11 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
12 | Impedance mismatch between the reference antenna and the network analyzer. | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
13 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
14 | Polarization mismatch for reference antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
15 | Mutual coupling between the reference antenna and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
16 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
17 | Uncertainty of the network analyzer | 0.13 | 0.2 | Gaussian | 1 | 1 | 0.13 | 0.2
18 | Influence of the reference antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
19 | Reference antenna feed cable loss measurement uncertainty | 0.06 | 0.06 | Gaussian | 1 | 1 | 0.06 | 0.06
20 | Influence of the receiving antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
21 | Uncertainty of the absolute gain of the reference antenna | 0.5 | 0.5 | Rectangular | √3 | 1 | 0.29 | 0.29
22 | Uncertainty of the absolute gain of the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  | 1.21 | 2.13
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  | 2.37 | 4.17
 | SE |  |  |  |  |  | 0.75 | 0.75
 | MU total |  |  |  |  |  | 2.5 | 4.2

## Slide 11: Additional requirements- co-existence
Requirement |  | Unit | Conducted MU |  |  | Conducted TT |  |  | OTA MU |  |  |  |  |  |  |  |  |  |  |  |  |  |  | OTA TT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Name | WF ref |  | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz | 3.0 GHz < f ≤ 4.2 GHz | 4.2 GHz < f ≤ 6.0 GHz | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  |  | f ≤ 3.0 GHz |  |  |  |  | 3.0 GHz < f ≤ 4.2 GHz |  |  |  |  | 4.2 GHz < f ≤ 6.0 GHz |  |  |  | 
 | c |  | AAS | AAS | E-UTRA | AAS | AAS | E-UTRA | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  |  | AAS |  |  |  | 
Company | c |  |  |  |  |  |  |  | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree | HW | NOK | E | Doc | Agree
6.7.6.4 Transmitter spurious emissions, Additional spurious emission requirements (3GPP co-existence) | 4 | dB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
> -60dBm, f ≤ 3.0GHz | 4 |  | 2.0 |  |  | 0 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  |  | x |  | 1.2 |  | 
> -60dBm, 3.0GHz < f ≤ 4.2GHz | 4 |  | 2.5 |  |  |  |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  |  | x |  | 1.4 |  | 
> -60dBm, 4.2GHz < f ≤ 6.0GHz | 4 |  | 3.0 |  |  |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  | 
> -60dBm, 6.0GHz < f ≤ 26.0GHz | 4 |  | x | x | x |  |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  |  | x |  | 1.6 |  | 
≤ -60dBm, f ≤ 3.0GHz | 4 |  | 3.0 |  |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  |  |  | 3.4 |  |  | 0 |  | 3.4 |  |  | 0 |  | 3.4 |  |  | 0 | 
≤ -60dBm, 3.0GHz < f ≤ 4.2GHz | 4 |  | 3.5 |  |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  |  |  | 3.9 |  |  | 0 |  | 3.9 |  |  | 0 |  | 3.9 |  |  | 0 | 
≤ -60dBm, 4.2GHz < f ≤ 6.0GHz | 4 |  | 4.0 |  |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  | 
≤ -60dBm, 6.0GHz < f ≤ 26.0GHz | 4 |  | x | x | x |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  |  | x |  |  |  | 
Mandatory additional e.g. PHS | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12: Additional requirements- co-existence
As with all the co-existence bands are 3GPP the MU’s are split in freq like the wanted signal – this can be kept.
The co-existence requirements (like the Rx emissions) are at a much lower power level so TRP calculation may be affected by the noise floor of the measurement system, the following definition is proposed:
Measurement system dynamic range uncertainty – uncertainty due to the test requirement being close to the measurement equipment noise floor and the noise floor contributing significantly to the TRP total.
Conducted MU are given for above and below -60dBm, the requirement levels are above -60dBm but the measured power for OTA will be less than -60dBm. As some contributions are lower than the conducted MU to keep the MU down the above -60dBm conducted values are used.

## Slide 13: Additional requirements- co-existence
Bvased on CATR as this is worst case for EIRP measurement (other can be sdone bit will be lower MU).
Measurement system dynamic range uncertainty added as low power level
SE added at 2σ
Proposal
  f ≤ 3 GHz, MU=2.5dB
  3 GHz < f ≤ 4.2 GHz, MU=2.5dB
    4.2 GHz < f ≤ 6 GHz, MU=2.9dB
UID | Uncertainty source | Uncertainty value |  |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] |  | 
 |  | f≤3 GHz | 3GHz<f ≤4.2GHz | 4.2GHz<f ≤6GHz |  |  |  | f≤3 GHz | 3GHz<f ≤4.2GHz | 4.2GHz<f ≤6GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  |  |  | 
1 | Misalignment DUT & pointing error | 0 | 0 | 0 | Exp. normal | 2 | 1 | 0 | 0 | 0
2 | Conducted measurement uncertainty (minus missmatch) | 1.02 | 1.02 | 1.28 | Gaussian | 1 | 1 | 1.02 | 1.02 | 1.28
3 | Standing wave between DUT and test range antenna | 0.21 | 0.21 | 0.21 | U-shaped | √2 | 1 | 0.15 | 0.15 | 0.15
4 | RF leakage, test range antenna cable connector terminated. | 0.0012 | 0.0012 | 0.0012 | Normal | 1 | 1 | 0.0012 | 0.0012 | 0.0012
5 | QZ ripple with DUT | 0.0928 | 0.0928 | 0.0928 | Normal | 1 | 1 | 0.0928 | 0.0928 | 0.0928
 | Measurement system dynamic range uncertainty | 0.51 | 0.51 | 0.51 | Gaussian | 1 | 1 | 0.51 | 0.51 | 0.51
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2 |  | 
Stage 1: Calibration measurement |  |  |  |  |  |  |  |  |  | 
6 | Network Analyzer | 0.13 | 0.2 | 0.2 | Normal | 1 | 1 | 0.13 | 0.2 | 0.2
7 | Uncertainty of return loss (S11) measurement of SGH and test receiver (VNA) ports | 0.127 | 0.325 | 0.325 | U-shaped | √2 | 1 | 0.09 | 0.23 | 0.23
8 | Insertion loss variation in receiver chain | 0.18 | 0.18 | 0.18 | Rectangular | √3 | 1 | 0.1 | 0.1 | 0.1
9 | RF leakage, test range antenna cable connector terminated. | 0.0012 | 0.0012 | 0.0012 | Normal | 1 | 1 | 0.0012 | 0.0012 | 0.0012
10 | Influence of the calibration antenna feed cable | 0.022 | 0.022 | 0.022 | U-shaped | √2 | 1 | 0.015 | 0.015 | 0.015
11 | SGH Calibration uncertainty | 0.5 | 0.433 | 0.433 | Rectangular | √3 | 1 | 0.29 | 0.25 | 0.25
12 | Misalignment positioning system | 0 | 0 | 0 | Exp. normal | 2 | 1 | 0 | 0 | 0
13 | Misalignment SGH and pointing error | 0.5 | 0.5 | 0.5 | Exp. normal | 2 | 1 | 0.25 | 0.25 | 0.25
14 | Rotary joints | 0.048 | 0.048 | 0.048 | U-shaped | √2 | 1 | 0.034 | 0.034 | 0.034
15 | Standing wave between SGH and test range antenna | 0.09 | 0.09 | 0.09 | U-shaped | √2 | 1 | 0.06 | 0.06 | 0.06
16 | QZ ripple with SGH | 0.009 | 0.009 | 0.009 | Normal | 1 | 1 | 0.009 | 0.009 | 0.009
17 | Switching uncertainty | 0.26 | 0.26 | 0.26 | Rectangular | √3 | 1 | 0.15 | 0.15 | 0.15
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  |  | 1.26 | 1.26 | 1.47
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  |  | 2.47 | 2.47 | 2.89