## Slide 1: Wayforward on dual SMTC periodicities
Mediatek
3GPP TSG-RAN WG4 RAN#88
Gothenburg, Sweden, 20th- 24th August, 2018
R4-1811688
Document for: Approval

## Slide 2: Background
  For intra-frequency CONNECTED mode measurement, UE can be configured with 2 SMTC with different periodicities.
  The RRC signaling is already provided in measurement object (MO) in TS38.331
    smtc2 is optional.
    If smtc2 is provided, a pci-List is also signaled to inform UE of which cell(s) is associated with this different periodicity.
    For all the other cells not listed in the pci-List, UE assumes their SMTC periodicity following smtc1.
    Periodicity of smtc1 is longer than smtc2.
  Not only the intra-frequency measurement requirement on the frequency layer with dual STMC periodicities will be impacted by which SMTC periodicity is selected, but also other requirements will be impacted.

## Slide 3: Wayforward
RAN4 to decide in the next meeting on which SMTC periodicity is assumed in a intra-frequency layer in below requirements
  Category A: Intra-frequency measurement requirements on the frequency layer with dual SMTC periodicities
  Category B: Other RRM requirements confirmed that is impacted

## Slide 4: Wayforward
  Possible list of category B requirements
    In TS 38.133
      8.2.1.2.5.1 Interruptions during measurements on deactivated NR SCC
      8.5 Link Recovery Procedures
      9.2 NR intra-frequency measurements
        9.2.5.3 Scheduling availability of UE during intra-frequency
      9.3 NR inter-frequency measurements
      9.4 Inter-RAT measurement measurements
      8.1 Radio link monitoring
    In TS 36.133
      8.17.3 E-UTRA Inter-frequency Measurements when configured with EN-DC Operation
      8.17.4 E-UTRA Inter-RAT NR Measurements when Configured with EN-DC Operation
  Companies are encouraged to confirm the list of requirements are impacted by dual SMTC periodicities

## Slide 5: For information
  For example, if NW configures 2 intra-frequency MOs to UE, then there could be up to 4 combinations due to the selection between smtc1 and smtc2.
The requirement of intra-F1 is impacted by the choice in intra-F2 and vice versa. Therefore totally the requirement of intra-F1 still has 4 cases
The requirement of inter-F3 is also impacted and has 4 cases
 | Intra-F1 | Intra-F2
Case 1 | smct1 | smct1
Case 2 | smct1 | smct2
Case 3 | smct2 | smct1
Case 4 | smct2 | smct2
Intra-F1, smtc1
Intra-F1, smtc2
Intra-F2, smtc1
Intra-F2, smtc2
Inter-F3, smtc
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
SSB
  An principle is needed to define a unique requirement for each measurement requirement (including intra-frequency layer itself and impacted intra/inter-frequency layers)

## Slide 6: Wayforward
  RAN4 to discuss which options will be used to define the requirements:
    Option 1: Both Category A and Category B assume smtc1
    Option 2: Both Category A and Category B assume smtc2
    Option 3:
      Category A always assumes smtc1
      Category B always assumes smtc2
    Option 4:
      Scenario-based rule, e.g., Example shown in the next page
    Option 5:
      Category A assumes the configured smtc1 or smtc2 depending on PCI
      Category B: FFS

## Slide 7
Table 1: SMTC periodicity that Category B assumes based on the collision status between SMTC occasions of Category A and MG. Measurement within MG might include Type A/B/C/D and measurement outside MG might include Type A/B.
 |  | Smtc2 |  | 
 |  | Fully overlapped | Partially overlapped | Fully non-overlapped
Smtc1 | Fully overlapped | Meas. within MG smtc2 | Meas. within MG smtc1 | N/A
 |  | Meas. outside MG N/A | Meas. outside MG smtc2 | 
 | Partially overlapped | N/A | Meas. within MG N/A | N/A
 |  |  | Meas. outside MG smtc2 | 
 | Fully non-overlapped | N/A | Meas. within MG N/A | Meas. within MG N/A
 |  |  | Meas. outside MG smtc2 | Meas. outside MG smtc2
  Scenario-based rules:
  Category A always assumes smtc1
  SMTC periodicity that Category B assumes based on Table 1

## Slide 8: Annex: dual SMTC periodicity of intra-frequency
  For intra-frequency CONNECTED mode measurement, UE can be configured with 2 SMTC with different periodicities.
  The RRC signaling is already provided in measurement object (MO) in TS38.331 through smtc1 and smtc2, as captured below.
smtc1 SEQUENCE { periodicityAndOffset CHOICE { sf5 INTEGER (0..4), sf10 INTEGER (0..9), sf20 INTEGER (0..19), sf40 INTEGER (0..39), sf80 INTEGER (0..79), sf160 INTEGER (0..159) }, duration ENUMERATED { sf1, sf2, sf3, sf4, sf5 } }, smtc2 SEQUENCE { pci-List SEQUENCE (SIZE (1..maxNrofPCIsPerSMTC)) OF PhysCellId OPTIONAL, -- Need M periodicity ENUMERATED {sf5, sf10, sf20, sf40, sf80, sf160, spare2, spare1} } OPTIONAL,-- Cond IntraFreqConnected

## Slide 9: Annex: dual SMTC periodicity of intra-frequency
  In the intra-MO, smtc2 is optional. If smtc2 is provided, a PCI list will also be signaled to inform UE of which cell(s) is associated with this different periodicity.
  For all the other cells not listed in the PCI-List, UE assumes their SMTC periodicity following smtc1.
  According to RAN1 agreement in NR#2 meeting, the periodicity of smtc1 is longer than smtc2.
Agreements: • Regarding the SS block based RRM measurement timing configuration (SMTC) i.e., measurement window periodicity/duration/offset information for UE RRM measurement per frequency carrier, – For intra-frequency CONNECTED mode measurement, up to two measurement window periodicities can be configured • UE can be informed of which cell(s) is associated with which measurement window periodicity • For cell(s) that is not listed, longer measurement window periodicity is used • Single measurement window offset and duration are configured per frequency carrier <Remaining parts omitted.>

## Slide 10: Annex: dual SMTC periodicity of intra-frequency
  in current TS38.133 spec, the requirement is cell-specified
  in Table 9.2.5.1-1
    For cells listed in the PIC list of smtc2, the requirement follows smtc2 (shorter periodicity).
    For cells not listed in the PIC list of smtc2, the requirement follows smtc1 (longer periodicity).
  In real field, it is possible that UE detects some cells associated with smtc1 and some associated with smtc2. In this case, UE needs to choose a SMTC period in this frequency layer.
DRX cycle | TPSS/SSS_sync
No DRX | max[ 600ms, ceil( [5] x Kp) x SMTC period ]Note 1
DRX cycle≤ 320ms | max[ 600ms, ceil(1.5x [5] x Kp) x max(SMTC period,DRX cycle) ]
DRX cycle>320ms | Ceil([5] x Kp) x DRX cycle
Note 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 
Table 9.2.5.1-1: Time period for PSS/SSS detection, (Frequency range FR1)