## Slide 1: Way forward on MRTD and MTTD for inter-band NR CA between FR1 and FR2
Ericsson, Nokia, ZTE, CATT, Verizon, KDDI, Vodafone, AT&T, Orange, T-Mobile Inc, NTT Docomo, [ … ]
3GPP TSG-RAN4 Meeting #88
Gothenburg, Sweden, 20 - 24 Aug 2018
R4-1811711

## Slide 2: Background
MRTD and MTTD for inter-band NR CA in FR1 and inter-band NR CA in FR2 are specified.
  MRTD and MTTD for inter-band NR CA between FR1 and FR2 is still open.
MRTD is directly related to allowed deployment flexibility for the operators
Two proposals for MRTD
  R4-1810926: 33µs
    Corresponds to 30µs of relative propagation delay difference and 3µs of BS TAE
  R4-1810321: 8µs
    Corresponds to 5µs of relative propagation delay difference and 3µs of BS TAE

## Slide 3: Deployment flexibility (1)
One main reason for CA deployment is to provide high capacity, low latency and high user throughput in hotspot areas with a high service demand through a high band with robust contiguous C-plane coverage using lower band NR.

## Slide 4: Deployment flexibility (2)
The MRTD (and MTTD) must therefore be sufficiently large not to restrict the deployment of NR base stations
  if it is too strict, it would limit the deployments of CA between high band cells (e.g. mmWave cells) and low band NR cells to be co-located at the same site.

## Slide 5: Issue-1: UE memory requirement
R4-1810321: claims “significantly higher UE memory overhead required due to 33µs of MRTD compared to 8µs”
TS 36.214: “µUL corresponds to the subcarrier spacing of the uplink channel with which the HARQ-ACK is to be transmitted”
  µUL is the total UL processing time
  Since FR1 is based 15kHz, and FR1 is Pcell, the total processing time is ~927µs
Conclusion
  Additional memory requirement is insignificant (i.e. 25µs vs 927µs)
  An additional MRTD of ~25µs should not have any significant impact on the UE HARQ storage, since other timing delay related portions are more significant (details in R4-1810926).

## Slide 6: Issue-2: UE buffer requirement due to Cross carrier scheduling
In cross carrier scheduling, grants for FR2 is received at FR1
Example: FR1 on 15kHz (1ms slot) and FR2 on 120kHz (125µs slot)
  Grants for FR2 slots 0-7 is sent via FR1 slot X; similarly grants for FR2 slots 8-15 are sent via FR1 slot X+1.
  1-3 symbols (71~213µs) PDCCH in FR1 are required for PDCCH decoding
In all cases below, maximum 2 slots of data needs to be stored
Conclusion: this buffer requirement does not depend on MRTD
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
X
X+1
FR1 PDCCH decoding time
Ex-1: no MRTD
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ex-2: FR1 leading
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ex-3: FR2 leading
FR1 PDCCH decoding time
1ms
1ms
FR1
FR2

## Slide 7: Issue-3: UL power control
UE is aware of slot pairs between FR1 and FR2
Regardless of MTTD, PCMAX pairs will be:
  Slot X in FR1 and slots 0-7 in FR2
  Slot X+1 in FR1 and slots 8-15 in FR2
Conclusion: PCMAX pairs are known to UE and regardless of any MTTD, UE will calculate PCMAX based on the PCMAX pairs
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
X
X+1
Ex-1: no MRTD
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ex-2: FR1 leading
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Ex-3: FR2 leading
PCMAX calculation window
1ms
1ms
PCMAX calculation window
FR1
FR2

## Slide 8: Proposal
Define MRTD as 33µs for inter-band NR CA between FR1 and FR2
Define MTTD as 34.1µs for inter-band NR CA between FR1 and FR2
  Reference: R4-1810927