## Slide 1: WF on MU and TT for transmission in-band TRP emission and directional requirements for FR2
Ericsson
R1-1811635

## Slide 2: Directional requirements
Frequency error: MU = 12Hz, TT = 12Hz (FR1 & FR2)
TAE: MU = 25 us TT = 25us (FR1 & FR2)
EVM: MU = 1%, TT = 1% (FR1 & FR2)
Output power dynamic range = MU 0.4dB, TT = 0.4dB (FR1 and FR2)
OBW: MU = 600kHz for 50MHz, [600] kHz for 100MHz, [600] kHz for 200MHz, [600] kHz for 400MHz, TT = 0 (FR2)

## Slide 3: EIRP accuracy for FR2
MU = 1.7dB (28GHz), 2.0dB (39GHz)
  These figures assume a power meter or calibrated spectrum analyzer
  The calibration procedure will be documented in the TR
TT = MU
Measurement budget as in Annex

## Slide 4: BS output power for FR2
MU = 2.1dB (28GHz), 2.4dB (39GHz)
  These figures assume a power meter or calibrated spectrum analyzer
  The calibration procedure will be documented in the TR
  Assumption of SE=1.2dB
TT = MU
Uncertainty budget is shown in the annex

## Slide 5: OBUE and absolute ACLR
MU = 2.7dB
  These figures assume a calibrated spectrum analyzer
    Instrument uncertainty 0.9 consisting of 0.7dB power meter and around 0.5dB residual uncertainty (0.9 is calculated as RSS)
  The calibration procedure will be documented in the TR
  Assumption of SE=1.2dB
OBUE: TT=MU for first 10%, TT=0 after first 10%
Absolute ACLR: TT = MU if no change in the core requirement (if core requirement changed to measurement bandwidth CBW then TT=0)
Note: Both requirements are specified as dBm/MHz and measured with the same equipment setup and MU
Uncertainty budget is shown in the annex

## Slide 6: Relative ACLR
MU = 1.8dB (28GHz), 2.4dB (39GHz)
  These figures assume a calibrated spectrum analyzer
    Instrument uncertainty 0.9 consisting of 0.7dB power meter and around 0.5dB residual uncertainty (0.9 is calculated as RSS)
  The calibration procedure will be documented in the TR
  Assumption of SE=1.2dB
TT = MU
Uncertainty budget captured in annex