## Slide 1: WF on how to handle CBW set for n77C, n78C, and n79C
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #88 R4-1811794
Gothenburg, Sweden, 20th – 24th August, 2018

## Slide 2: Background
To specify required CBW configuration, adding the below CBW for n77C, n78C, and n79C in Rel-15:
  10 MHz + 100 MHz
  20 MHz + 100 MHz
  40 MHz + 100 MHz
For the proposal, several comments were raised
  Comment 1: There is concern about impact on UE implementation in Rel-15
  Comment 2: Need to check necessity to specify the additional Rx requirements to adjust to new CBW set

## Slide 3: Way forward
Comment 1: There is concern about impact on UE implementation in Rel-15
Comment 2: Need to check necessity to specify the additional Rx requirements to adjust to new CBW set
Company are encourage to clarify the feasibility of adding new CBW in Rel-15 by next meeting
  If it is acceptable, apply Option 1 (new CBW set is specified in Rel-15)
    No additional Rx requirement are needed, because:
      Current Rx requirement is specified based on aggregated BW of CA
      Corresponding aggregated CBW for Rx requirements are already exist in spec
  If it is not acceptable, apply Option 2 (new CBW set is specified in Rel-16)
    Evaluate additional Rx requirements to adjust to new CBW set
    Using Release-independent approach should be considered
Option 1 | Rel-15
Option 2 | Rel-16

## Slide 4: References
[1] R4-18010730 Draft CR for maintenance for CBW set on n77C, n78C, and n79C for TS 38.101-1, DOCOMO, INC., RAN4#88