## Slide 1: Way forward on intra and inter frequency measurement requirements in DRX mode
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, CN, 8th – 12th Oct, 2018
R4-1813725
Document for: Approval

## Slide 2: Background
MN and SN can configure DRX mode to MCG and SCG separately for NR DC case such as LTE DC case.
  Following cases can be considered.
RAN4 needs to define the principle of measurement requirements for case B, C, D.
  Focusing on EN-DC case.
  NE-DC and NR-NR DC will be discussed later.
 | DRX On/Off | 
 | DRXMN | DRXSN
Case A | OFF | OFF
Case B | ON | OFF
Case C | OFF | ON
Case D | ON | ON

## Slide 3: Wayforward
In RAN4#88bis, companies have different views on this issue.
For RAN4#89, companies encourage to input on how to define the principle.
Some options proposed in RAN4#88bis are provided from next slide. Investigate of other options are not precluded.

## Slide 4: Wayforward
In case of EN-DC,
  For intra-frequency measurement requirements in DRX mode on LTE PCell or LTE SCells in MCG,
    If MCG DRX is in use, then the LTE intra-frequency requirements for when DRX is in use shall apply and shall depend on the MCG DRX cycle duration.
    Otherwise, the requirements for when DRX is not in use shall apply.
  For intra-frequency measurement requirements in DRX mode on NR PSCell or NR SCells in SCG,
    If SCG DRX is in use, then the NR intra-frequency requirements for when DRX is in use shall apply and shall depend on the SCG DRX cycle duration.
    Otherwise, the requirements for when DRX is not in use shall apply.
  For RLM and BFD in DRX mode,
    UE follows the same principle as above.

## Slide 5: Wayforward
When both MCG and SCG DRX are in use and different value of DRX cycle is configured between MCG and SCG
  If MCG DRX cycle and SCG DRX cycle ≥40ms,
    Option1: Measurement requirements apply larger value of DRX cycle.
      Both intra and inter frequency measurements apply above.
    Option2:Measurement requirements apply shorter value of DRX cycle.
      Both intra and inter frequency measurements apply above.

## Slide 6: Wayforward
When both MCG and SCG DRX are in use and different value of DRX cycle is configured between MCG and SCG
  If MCG DRX cycle or SCG DRX cycle <40ms,
    Option1:
      LTE inter-frequency and NR inter-RAT requirements shall follow MGC DRX cycle duration and state.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state..
    Option2:
      LTE inter-frequency requirements shall follow MGC DRX cycle duration and state
      NR inter-RAT requirements shall follow larger value of DRX cycle configured between MCG and SCG.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state.
    Option3:
      LTE inter-frequency requirements shall follow MGC DRX cycle duration and state.
      NR inter-RAT requirements shall follow SCG DRX cycle duration and state.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state.

## Slide 7: Wayforward
If MCG or SCG are in non-DRX,
    Option1:
      LTE inter-frequency and NR inter-RAT requirements shall follow MGC DRX cycle duration and state.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state..
    Option2:
      LTE inter-frequency requirements shall follow MGC DRX cycle duration and state
      NR inter-RAT requirements shall follow larger value of DRX cycle configured between MCG and SCG.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state.
    Option3:
      LTE inter-frequency requirements shall follow MGC DRX cycle duration and state.
      NR inter-RAT requirements shall follow SCG DRX cycle duration and state.
      NR inter-frequency requirements shall follow SGC DRX cycle duration and state.

## Slide 8: Reference
R4-1812710, Inter-frequency measurement requirements in DRX modes, NTT DOCOMO, INC.
R4-1812502, Discussion on inter-frequency requirements, MediaTek inc.