## Slide 1: 3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 8 – 12 October 2018
Huawei, HiSilicon, Nokia
Way forward on NR beam management
R4-1813736

## Slide 2: Existing agreements on BFD
The agreement on BFD from RAN4#88bis main session
  The value of BLERout used for BFD evaluation is 10%.

## Slide 3: Way forward on BFD
Companies are encouraged to confirm the support of SSB based BFD with RAN1 by RAN4#89.
  The requirements for SSB based BFD will be removed if SSB based BFD is not supported.
For SSB (if supported) and CSI-RS based BFD, N (scaling factor for beam sweeping) is fixed to 8 when condition for N=1 does not apply
FFS if requirements for D=1 with larger BW are defined for CSI-RS based BFD
FFS UE behaviour concerning UL transmission when beam failure is detected

## Slide 4: Way forward on BFD (cont)
For SSB based BFD (if supported), FFS if N=1 is feasible and under which condition
For CSI-RS based BFD, FFS the condition for N=1. Consider at least the following factors to define the condition
  Whether repetition is configured for the CSI-RS resource set to which the CSI-RS for BFD belongs to
  Whether the TCI state is configured for the CSI-RS resource with reference to other RS for L1-RSRP reporting with QCL-Type D

## Slide 5: Existing agreements on CBD
The agreement on CBD from RAN4#88bis AH session
  -3dB as side condition for CBD measurement.
  For CSI-RS based CBD, CSI-RS is assumed to be transmitted in >=24 PRBs with D=3
  [3] samples for SSB and [5] samples for CSI-RS with D=3 with FFS accuracy, FFS how to capture the accuracy requirements in the spec
  FFS if requirements for D=1 with larger BW are defined.
  CBD measurement may cause scheduling restriction when performed. When CBD measurement is performed is FFS.
    Option 1: CBD measurement is performed only when beam failure is detected
    Option 2: Up to UE implementation
  FFS if N=1 can apply when SSB is included in SMTC.
  No other is no condition for N=1 for SSB based CBD measurement
  FFS if N=1 can apply for CSI-RS based CBD measurement and if so what is the condition
  N is fixed to 8 when condition for N=1 does not apply.
  Same scheduling restriction due to CBD measurement are defined as for L1-RSRP for beam reporting
  FFS prioritization between L3 measurement in SMTC and CBD measurement.

## Slide 6: Way forward on CBD
For SSB based CBD, FFS if N=1 is feasible under the condition that SSB is included in SMTC
For CSI-RS based CBD, FFS if N=1 is feasible and the condition
FFS if requirements for D=1 with larger BW are defined for CSI-RS based CBD
FFS when UE scheduling restriction are allowed due to CBD measurement being performed.
  Option 1: when beam failure is detected
  Option 2: Up to UE implementation
FFS prioritization between L3 measurement in SMTC and CBD measurement.

## Slide 7: Existing agreements on L1-RSRP measurement for beam reporting
The agreement on beam reporting from RAN4#88bis main session
  The measurement requirement for L1-RSRP reporting will be specified.
  follow the same agreement as for CBD for scaling factor value for SSB and CSI-RS based beam reporting.
  The scaling factor P of L1 measurement/evaluation period due to colliding with MG, P factor specified for CBD evaluation period is reused

## Slide 8: Way forward on beam reporting
FFS if L1 averaging for L1-RSRP measurement for beam reporting should be specified.
L1-RSRP measurement accuracy requirements are defined based on single-shot measurement and [-3]dB SNR side condition.
  FFS if other accuracy requirements based on averaging are defined
FFS requirements for L1-RSRP measurement for beam reporting are defined for aperiodic and semi-persistent reporting.
For SSB based L1-RSRP measurement, [N=1 does not apply]
For CSI-RS based L1-RSRP measurement, FFS if N=1 is feasible and the condition
For SSB based L1-RSRP measurement, the scaling factor P due to colliding with MG and SMTC, is reused from P factor defined for BFD.
For CSI-RS based L1-RSRP measurement, the scaling factor P due to colliding with MG and SMTC is FFS.
FFS the number of SSB and CSI-RS resources UE is required to monitor in the serving cell
FFS if requirements for D=1 with larger BW are defined for CSI-RS based CBD