## Slide 1: WF on the maximum CCs of contiguous FR2 UL CA in Rel-15
NTT DOCOMO, INC., Verizon, KDDI, T-Mobile,
Nokia, SK telecom, Qualcomm Incorporated
R4-1813861

## Slide 2: Background
In RAN4#88, the scope of intra-band contiguous UL CA in Rel-15 was further clarified as the maximum aggregated BW is up to 800MHz
  which was approved in updated Rel-15 Work Item Exception in RAN#81[1].
In this meeting, there are proposals for further clarification as below:
  Scope of the maximum CCs is 8 CCs [2-4]
  EN-DC including NR UL CA in FR2 proposed later than Rel-15 can apply release-independent approach from Rel-15 [2,3]
However, several concerns are raised
  For scope of the maximum CCs, it should be up to 2, or 4.
  Whether release-independent approach can be applied or not should be discussed

## Slide 3: Way forward
Option 1: Scope of maximum CCs in Rel-15 is 8CCs
Option 2: Scope of maximum CCs in Rel-15 is at least 4CCs, and 8CCs will be concluded by RAN4#89. Missing requirement for 8CCs is continue to be discussed.
Way forward
Apply the Option 1
  There are market demand to use 8CCs with aggregated BW is 800MHz. If there are no requirements for 8CCs, UE can not support 8CCs as Rel-15 feature.
  8CCs NR FR2 UL contiguous CA combinations with maximum aggregated BW = 800 MHz are already proposed as release independent from Rel-15 in the approved WID[5].
EN-DC including NR UL contiguous CA in FR2 proposed later than Rel-15 can apply release-independent approach from Rel-15.
  EN-DC combinations including 8CCs NR FR2 UL contiguous CA with maximum aggregated BW = 800MHz are also already proposed in the approved WID[6-9].

## Slide 4: Reference
[1] RP-182083, “Rel-15 Work Item Exception for New Radio Access Technology – Core”, NTT DOCOMO, INC. , RAN#81, Gold Coast, Australia, September 10-13, 2018
[2] R4-1812193, “Scope of FR2 ULCA in Rel-15”, Qualcomm Incorporated, Verizon, Nokia, Telecom Italia, AT&T, RAN4#88bis, Chengdu, China, October 8-12, 2018.
[3] R4-1813068, “NR UL CA for FR2 in Rel-15”, NTT DOCOMO, INC., RAN4#88bis, Chengdu, China, October 8-12, 2018.
[4] R4-1812196, “CA in FR2”, Intel Corporation, RAN4#88bis, Chengdu, China, October 8-12, 2018.
[5] RP-181549, “Revised WID: Rel-16 NR intra band Carrier Aggregation for xCC DL/yCC UL including contiguous and non-contiguous spectrum (x>=y)”, Ericsson, 3GPP TSG RAN meeting #81, Gold Coast, Australia, September 10-13, 2018
[6] RP-181885, “Revised WID: Dual Connectivity (EN-DC) of 1 LTE band (1DL/1UL) and 1 NR band (1DL/1UL)”, NTT DOCOMO, INC., 3GPP TSG RAN meeting #81, Gold Coast, Australia, September 10-13, 2018
[7] RP-181855, “Revised WID: EN-DC for 3 bands DL with 2 bands UL (2 LTE bands + 1 NR band)”, Huawei, HiSilicon, 3GPP TSG RAN meeting #81, Gold Coast, Australia, September 10-13, 2018
[8] RP-181550, “Revised WID: Dual Connectivity (EN-DC) of 3 bands LTE inter-band CA (3DL/1UL) and 1 NR band (1DL/1UL)”, Ericsson, 3GPP TSG RAN meeting #81, Gold Coast, Australia, September 10-13, 2018
[9] RP-181834, “Revised WID: Dual Connectivity (EN-DC) of 4 bands LTE inter-band CA (4DL/1UL) and 1 NR band (1DL/1UL)”, Nokia, Nokia Shanghai Bell, 3GPP TSG RAN meeting #81, Gold Coast, Australia, September 10-13, 2018