## Slide 1
WF on fractional BW
NEC
R4-1813871
3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 8th – 20th October, 2018
Agenda item: 7.8.3.1

## Slide 2
Current status
FBW is adopted to EIRP requirement [1], [2]
  FBW definition: based on highest and lowest frequencies of the operation band
  Threshold to declare multiple EIRP values: FBR > 6%
  Number of EIRP declarations when FBR condition is met : 2
    EIRPFBWlow at minimum supported frequency FFBWlow and EIRPFBWhigh at maximum supported frequency FFBWhigh
    EIRPFBWlow, for the frequency range FFBWlow ≤ f < (FFBWlow +FFBWhigh) / 2,
    EIRPFBWhigh, for the frequency range (FFBWlow +FFBWhigh) / 2 ≤ f ≤FFBWhigh
Related discussion
  Background information to introduce FBR [3]: noted
  Modification of FBW definition and EIRP declarations [4]: noted
  FBR introduction to OTA base station output power [5]: noted
  FBR introduction to base station output power [6]: noted

## Slide 3
Way Forward
Companies are encouraged to provide their view in RAN4#89
Details of the FBW operations
  FBW definition
    Option 1: Based on operating band (current)
    Option 2: Based on supported band
    Option 3: Others
  FBW threshold to adopt multiple declarations/sub-bands
    Option 1: 6% (current)
    Option 2: Others
  Number of declarations/sub-bands to be introduced
    Option 1: 2 (current)
    Option 2: 3
    Option 3: Others
Regulatory impacts

## Slide 4
Way Forward
Companies are encouraged to provide their view in beyond RAN4#89
Background to introduce FBW
  Antenna directivity
  Antenna efficiency
  Power amplifier
  Filter
  Others
Applicability of FBW feature (scenario)
  Carrier aggregation cases
  Multi-band cases
  Wider channel bandwidth (which could be introduced in the future)
Applicability of FBW feature (RAT)
  NR (FR1 conducted, FR1 OTA, FR2 OTA)
  AAS (conducted, OTA)
  MSR
Applicability of FBW feature (Requirements)
  Radiated transmit power (current)
  OTA base station output power
  Base station output power
  Others

## Slide 5
References
[1] R4-1808484, Draft CR for TS 38.104: Improvement of declarations for wide NR bands in sub-clause 9.2, Ericsson
[2] R4-1811583, Draft CR to TS 38.104: wideband operation and fractional bandwidth corrections (9.2.1), Huawei
[3] R4-1812900, CR for TR 38.817-02: Adding missing background information for radiated transmit power in sub-clause 9.2.1, Ericsson
[4] R4-1813715, Draft CR for TS 38.104: Radiated transmit power requirement with wideband operation (9.2), NEC
[5] R4-1813179, Draft CR for TS 38.104: OTA base station output power with wideband operation (9.3), NEC
[6] R4-1813177, Draft CR for TS 38.104: Base station output power requirement with wideband operation (6.2), NEC