## Slide 1: WF on RF channels for OTA testing
Nokia, Nokia Shanghai Bell, Huawei…
R4-1813878
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8-12 October 2018

## Slide 2: Background
During RAN4#88bis meeting the following contributions were discussed:
[1] R4-1813564 RF channels for NR OTA tests Nokia, Nokia Shanghai Bell
[2] R4-1812684 Discussion on RF channels for OTA testing Huawei, HiSilicon
[3] R4-1812604 TP for TS38.141-1: Adding a note for some specific requirements on RF channel, ZTE Corporation
[4] R4-1812758 pCR to TS 38.141-1 : Test Cases position update for IM and Blocking, Ericsson
[5] R4-1812605 TP for TS38.141-2: RF channel for BS OTA conformance test, ZTE Corporation
This document summarizes the way forward on RF channels for OTA conformance tests.

## Slide 3: Background (1/2)
During RAN#88 meeting following was agreed [1] for OTA RF channels:
Agreement:
For OTA, RF channel as conductive test can be used as starting point.
RF channels for conductive test are presented on the next slide.
[1] R4-1812001 RAN4#88 Meeting Report, Source: ETSI MCC

## Slide 4: Background (2/2)
Requirements |  | RF channels |  | 
 |  | single carrier | Multi-carrier | Multi-carrier, Multi-band
6.2 | BS output power | B,M,T | BRFBW, MRFBW, TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.3 | Total power dynamic range | M | - | -
6.4 | Transmitter ONN/OFF power | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.5.2 | Frequecny Error | Same as EVM | Same as EVM | Same as EVM
6.5.3 | Modulation quality | B,M,T | BRFBW, MRFBW, TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.5.4 | TAE | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.1 | Occupied BW | M | MBW Channel CA | -
6.6.2 | ACLR | B,M,T | BRFBW, MRFBW, TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.2.2 | CACLR (NC) | N/A | BRFBW, MRFBW, TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.4 | Operating band unwanted emissions | B,M,T | BRFBW, MRFBW, TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.5 | Transmitter spurious emissions | B for spurious frequencies below the band, T for frequencies above the band | BRFBW for spurious frequencies below the band, TRFBW for frequencies above the band | BRFBW_T'RFBW, B'RFBW_TRFBW
6.7 | Transmitter intermodulation | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.2 | Reference sensitivity level | B,M,T | - | -
7.3 | Dynamic range | M | - | -
7.4.1 | Adjacent Channel Selectivity(ACS) and narrow-band blocking | Option 1: B,M,T Option 2:M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.4.2 | In-band blocking | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.5 | Out of band bocking | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.6 | Receiver spurious emissions | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.7 | Receiver intermodulation | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.8 | In-channel selectivity | M | - | -
Already agreed RF channels for conductive (incorporated into TS 38.141-1)

## Slide 5: WF on RF channels for OTA tests
Clause | BS test requirement | Single carrier | Multi-carrier and/or CA in single band | Multi-band
6.2 | Radiated transmit power | B, M, T | BRFBW, MRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.3 | OTA base station maximum output power | B, M, T | BRFBW, MRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
 | OTA RE Power control dynamic range | Tested with Error Vector Magnitude | Tested with Error Vector Magnitude | Tested with Error Vector Magnitude
6.4.3 | OTA total power dynamic range | M | - MRFBW | -
6.5 | OTA transmit ON/OFF power (only applied for NR TDD BS) | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.2 | OTA frequency error | B, T | BRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.3 | OTA error Vector Magnitude | B, T | BRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.6.4 | OTA time alignment error | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.7.2 | OTA Occupied bandwidth | M | MBW Channel CA | - BRFBW_T'RFBW, B'RFBW_TRFBW
6.7.3 | OTA ACLR | B, T | BRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.7.4 | OTA operating band unwanted emissions | B, M, T | BRFBW, MRFBW and TRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
6.7.5 | OTA transmitter spurious emissions | As already defined in TS 38.141-2 v1.0.0 | As already defined in TS 38.141-2 v1.0.0 | As already defined in TS 38.141-2 v1.0.0
6.8 | OTA transmitter intermodulation | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.2 | OTA sensitivity | M | - MRFBW | -
7.3 | OTA reference sensitivity level | B, M, T | - BRFBW, MRFBW and TRFBW | -
7.4 | OTA dynamic range | M | - MRFBW | -
7.5.1 | OTA adjacent channel selectivity | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.5.2 | In-band blocking | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.6 | OTA out-of-band blocking | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.7 | OTA receiver spurious emissions | As already defined in TS 38.141-2 v1.0.0 | As already defined in TS 38.141-2 v1.0.0 | As already defined in TS 38.141-2 v1.0.0
7.8 | OTA receiver intermodulation | M | MRFBW | BRFBW_T'RFBW, B'RFBW_TRFBW
7.9 | OTA in-channel selectivity | M | - MRFBW | -
Following RF channels are agreed to be used for OTA FR1 and OTA FR2 tests: