## Slide 1: WF for SSB-based RLM test cases in Rel-15
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #88-Bis
Chengdu, China, 8th – 12th Oct, 2018
Agenda Item: 7.12.5.13
Document for: Approval
R4-1813987

## Slide 2: Background – Agreement in ad-hoc session
Propagation channel: only fading channels.
BFR-triggered RLF Avoidance
  BFR-triggered RLF should be avoid.
  Option 1: largest preambleTransMax value, the longest periodicity of PRACH occasion and larger ra-ResponseWindow for BFR
    preambleTransMax = [n200]
    periodicity of PRACH occasion = [160]ms
    ra-ResponseWindow = [1] slot for FR1 and [40] slots for FR2
Have PRACH configurations defined in the common part which we can referred to for each test.
Reuse LTE RLM test methodology with some modifications
  OOS: Time difference between point B and point C (T4) shall equal to TEvaluate_out + 40 ms
  INS:
    T3 > TEvaluate_out
    T310 >= T3+T4+TEvaluate_in + SSB burst duration
    T6 > TEvaluate_out + T310 + 40 – T3 –T4

## Slide 3: Way forward(1)
Issue 1: List of RLM test cases in EN-DC. EUTRA is in non-DRX mode
A. 4.5.1.1 | FR1 | Non-DRX | OOS | w/o meas. gap | Test 1 (test config 1-6)
 |  |  |  | w/ meas. gap | Test 2 (test config 1-6)
A. 4.5.1.2 |  |  | INS | w/o meas. gap | Test 1 (test config 1-6)
 |  | DRX | OOS | w/o meas. gap | Test 1 (test config 1-6)
A. 4.5.1.3 |  |  |  |  | 
A. 4.5.1.4 |  |  | INS | w/o meas. gap | Test 1 (test config 1-6)
A.5.5.1.1 | FR2 | Non-DRX | OOS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
 |  |  |  | w/ meas. gap | Test 2: TDD SSB SCS 120KHz, data SCS 120KHz
A.5.5.1.2 |  |  | INS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
A.5.5.1.3 |  | DRX | OOS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
A.5.5.1.4 |  |  | INS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
Configuration | Description
1 | LTE FDD, NR 15 kHz SSB SCS, 10MHz bandwidth, FDD duplex mode
2 | LTE FDD, NR 15 kHz SSB SCS, 10MHz bandwidth, TDD duplex mode
3 | LTE FDD, NR 30kHz SSB SCS, 40MHz bandwidth, TDD duplex mode
4 | LTE TDD, NR 15 kHz SSB SCS, 10MHz bandwidth, FDD duplex mode
5 | LTE TDD, NR 15 kHz SSB SCS, 10MHz bandwidth, TDD duplex mode
6 | LTE TDD, NR 30kHz SSB SCS, 40MHz bandwidth, TDD duplex mode
Note: The UE is only required to pass in one of the supported test configurations in FR1 | 

## Slide 4: Way forward(2)
Issue 2: List of RLM test cases for SA
A. 6.5.1.1 | FR1 | Non-DRX | OOS | w/o meas. gap | Test 1 (test config 1-6)
 |  |  |  | w/ meas. gap | Test 2 (test config 1-6)
A. 6.5.1.2 |  |  | INS | w/o meas. gap | Test 1 (test config 1-6)
 |  | DRX | OOS | w/o meas. gap | Test 1 (test config 1-6)
A. 6.5.1.3 |  |  |  |  | 
A. 6.5.1.4 |  |  | INS | w/o meas. gap | Test 1 (test config 1-6)
A.7.5.1.1 | FR2 | Non-DRX | OOS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
 |  |  |  | w/ meas. gap | Test 2: TDD SSB SCS 120KHz, data SCS 120KHz
A.7.5.1.2 |  |  | INS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
A.7.5.1.3 |  | DRX | OOS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
A.7.5.1.4 |  |  | INS | w/o meas. gap | Test 1: TDD SSB SCS 120KHz, data SCS 120KHz
Configuration | Description
1 | LTE FDD, NR 15 kHz SSB SCS, 10MHz bandwidth, FDD duplex mode
2 | LTE FDD, NR 15 kHz SSB SCS, 10MHz bandwidth, TDD duplex mode
3 | LTE FDD, NR 30kHz SSB SCS, 40MHz bandwidth, TDD duplex mode
4 | LTE TDD, NR 15 kHz SSB SCS, 10MHz bandwidth, FDD duplex mode
5 | LTE TDD, NR 15 kHz SSB SCS, 10MHz bandwidth, TDD duplex mode
6 | LTE TDD, NR 30kHz SSB SCS, 40MHz bandwidth, TDD duplex mode
Note: The UE is only required to pass in one of the supported test configurations in FR1 | 

## Slide 5: Way forward(3)
Issue 3: The number of SSB in FR1 RLM test
  Option 1: 1
  Option 2: 2. FFS SNR point of the 2nd SSB.
Issue 4: The number of SSB in FR2 RLM test
  Option 1: 1
  Option 2: 2. FFS SNR point of the 2nd SSB.
Issue 5: N factor for evaluation period in FR2. (Strive to minimize the number of test case)
  Option 1: N= 1 for all test cases. FFS how to enable N=1.
  Option 2: N=8 for some cases
Issue 6: FFS whether to introduce gradually power changes on SSB
  Example. NB IoT RLM (e.g., TS36.133, A.7.3.60)

## Slide 6: Way forward (4)
Companies are encouraged to suggest SNR margin in the next meeting, based on the required SNR and SNR margin.
  SNR2 = Qout + margin_2
  SNR3 = Qout – margin_3
  SNR4 = Qin – margin_4
  SNR5 = Qin + margin_5
  SNR1 = SNR5
  Whether to have different margins for different SCS.
    Opt.1: yes
    Opt.2: for FR1 we can use the single margin
  Current aligned simulation results is provided in the last page for information
  Example template for SNR margin collection:
Reference symbols | SCS for ref symbol | SCS for PDCCH | Propagation channel | Margin_2 (dB) | Margin_3 (dB) | Margin_4 (dB) | Margin_5 (dB)
SS/PBCH | 15kHz | 15kHz | Fading (TDL-C 300ns, 100Hz) |  |  |  | 
 | 30kHz | 30kHz | Fading (TDL-C 300ns, 100Hz) |  |  |  | 
 | 120kHz / [240 kHz] | 120kHz | Fading (TDL-A 30ns, 75Hz) |  |  |  | 

## Slide 7: For information
According to the simulation results in R4-1812516, for fading channel (The median value is used for example.)
Test configuration | 2RX, Required SNR (dB) |  | 4RX, Required SNR (dB) | 
 | Qout | Qin | Qout | Qin
SSB SCS15KHz, data SCS15KHz | [-10.1] | [-1.8] | [-12.9] | [-5.5]
SSB SCS30KHz, data SCS30KHz | [-9.6] | [-1.7] | [-12.8] | [-5.3]
SSB SCS120KHz, data SCS120KHz | [-9.6] | [-0.8] | [-10.8] | [-3.9]
SSB SCS240KHz, data SCS120KHz | [-8] | [0] | [-10.7] | [-3.9]