## Slide 1: Way forward on demodulation performance for eV2X UE
3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 08-12 Oct , 2018
Agenda Item: 6.3.5
R4-1814021
CATT

## Slide 2: Background
The following agreements were captured in WF(R4-1811696):
  Define two additional PSSCH test cases with GNSS based synchronization:
    PSSCH, 20MHz, MCS[22], EVA[180], [8]RB, retransmission: 0 time
    PSSCH, 10MHz, MCS4, EVA2700, 3RB, retransmission: 1 time
  Define the following requirements for Rel-15 eV2X CA
    Define PSSCH soft buffer test
    PSCCH decoding capability test
    Sustained downlink data rate test
  Do not define UE performance requirements to verify transparent transmit diversity
  scheme feature.
  Do not define any UE performance requirements for Mode-3/Mode-4 pool sharing and Resource selection latency reduction features.

## Slide 3: Background
  The following agreements were reached in Tuesday main session:
  Use the following assumptions for Rel-15 eV2X normal PSSCH requirements definition for scenarios with 64QAM modulation:
    20MHz, MCS21, EVA180, 8RB, 1 retransmission, 600Hz Tx CFO
  Define Rel-15 eV2X soft buffer requirements for test point 12 dB.

## Slide 4: PSSCH enhancement
  eV2X PSSCH enhancement performance requirement
  Define two additional PSSCH test cases with GNSS based synchronization:
    PSSCH, 20MHz, MCS21, EVA180, 8RB, 1 retransmission
    PSSCH, 10MHz, MCS4, EVA2700, 3RB, 1 retransmission

## Slide 5: Soft buffer test
Background
  SL-C-Rx Category 3 and 4 have been introduced for Rel-15 eV2X UE
Test purpose
  Verify SL soft buffer management and the maximum number of bits per TTI supported by the UE
    single carrier with 20 MHz CBW to verify SL-C-RX Category 3
    3 CCs with 10MHz CBW to verify SL-C-RX Category 4
    2 CCs with 10MHz+20MHz CBW to verify SL-C-RX Category 4
Test point: 12dB
UE SL-C-RX Category | Maximum number of SL-SCH transport block bits received within a TTI | Maximum number of bits of a SL-SCH transport block received within a TTI | Total number of soft channel bits | Comments
SL-C-RX Category 1 | 25456 | 25456 |  | 
SL-C-RX Category 2 | 31704 | 31704 | 737280 | 20MHz aggregated BW 16QAM
SL-C-RX Category 3 | 48936 | 48936 | 995328 | 20MHz aggregated BW 64QAM (Applicable for 10MHz+10MHz and 20MHz)
SL-C-RX Category 4 | 24496 + 24496 + 24496 = 73488 | 48936 | 1492992 | 30MHz aggregated BW 64QAM (Applicable for 10MHz+10MHz+10MHz and 10MHz+20MHz)

## Slide 6: PSCCH decoding processing test
Background
  New PSCCH decoding capability has been introduced for Rel-15 eV2X UE
Test configuration
  Verify PSCCH decoding capability both X=15 and X=30 according to UE capability for CA scenarios with 2 and 3 CCs
Aggregated RX BW by UE, MHz | V2X High Reception Capability | V2X Default Reception Capability
10, 20 (Rel.14, Rel.15) | 20 PSCCHs and 136 RBs | 10 PSCCHs and 100 RBs
30 (Rel.15) | 30 PSCCHs and 204 RBs | 15 PSCCHs and 150 RBs

## Slide 7: Simulation assumptions
Single-link PSSCH test
  Evaluation cases
    PSSCH, 20MHz, MCS21, EVA180, 8RB, retransmission: 1 time
    PSSCH, 10MHz, MCS4, EVA2700, 3RB, retransmission: 1 time
      Time interval between initial transmission and retransmission equals to 8ms
  CFO and Doppler shift algorithms: “single-DMRS” estimation
  Channel estimation
    linear interpolation in time domain
    frequency domain MMSE equalization
  PSSCH frequency offset estimation
    PSSCH DMRS
  Adjacent RBs are allocated for SA and its associated PSSCH transmission in the
  same subframe
  Note: The above assumptions have been used in Rel-14 V2X.

## Slide 8: Simulation assumptions
Single-link PSSCH test
- Note: Interested companies are invited to provided simulation results in next meeting.
Parameters | Unit | Test 1 | Test 2
Bandwidth | MHz | 10 | 20
RB |  | 3 | 8
MCS |  | MCS4 | MCS21
Time offset |  | +24Ts | 
Frequency offset | Hz | +1200 | 
Propagation condition |  | EVA2700 | EVA180
Antenna configuration |  | 1x2 Low | 
Soft combining |  | Yes | 
Synchronization |  | GNSS or GNSS-equivalent | 
Table 1 Proposed simulation assumptions for PSSCH