## Slide 1: WF on UE behavior and network configuration without SCS restriction
Qualcomm, Huawei

## Slide 2: Background
RAN2 signal design for UE carrier BW and location
  Part of FreqInfoDL -> scs-SpecificCarrierList
    carrierBandWidth
    offsetToCarrier
  Since both carrier BW and offset are per SCS, the network can configure the UE with multiple carrierBW’s
Network can configure the UE with one or multiple carrierBandWidth’s
  At most one carrierBandWidth for each SCS

## Slide 3: BWP Configuration
For a UE to be configured with a BWP with a particular SCS, the carrierBandWidth for that SCS needs to be indicated to the UE

## Slide 4: Network Behavior
For two carrierBandwidths configured for two different SCS’s
  Scenario 1: The carrierBandwidth for two SCS’s do not overlap
  Scenario 2: The carrierBandwidth for two SCS’s partially overlap
  Scenario 3: The carrierBandwidth for one SCS is fully contained in the other
  Scenario 4: The carrierBandwidth for two SCS’s fully overlap

## Slide 5: Scenario Illustration
carrierBandwidth1, SCS1
carrierBandwidth BW2, SCS2
carrierBandwidthBW1, SCS1
carrierBandwidthBW2, SCS2
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
carrierBandwidth BW1, SCS1
carrierBandwidth BW2, SCS2
Scenario 1
Scenario 2
Scenario 3
Scenario 4
BWP1, SCS1
BWP2, SCS2
BWP1, SCS1
BWP1, SCS1
BWP1, SCS1
BWP2, SCS2
BWP2, SCS2
BWP2, SCS2

## Slide 6: Implications to UE Behavior
For scenarios 1 , 2 and 3 a BWP switch different SCS could also mean a carrierBandwidth switch.
  BWP switch times between non-overlapping carrierBandwidth may be in general larger than BWP switching delay within overlapping carrierBandwidth.
Network configuration in terms of Scenarios 1-4 would dictate UE behavior

## Slide 7: UE Behavior
Need to pick one option of UE behavior for each scenario
Option 1: UE needs to satisfy the requirements based on the carrierBandwidth corresponding to the SCS of the BWP
Option 2: Pick a reference carrierBandwidth /SCS
  Reference carrierBandwidth should span all configured BW
  RF requirements need to exist for the reference carrierBandwidth /SCS combination
Option 3: BWP switch here implies a CC switch. UE can declare RLF
Other options not precluded

## Slide 8: WF
WF
  1) Check if possible to narrow down which scenarios the network can deploy.
  2) Define UE behavior in each of the scenarios network can deploy
    Pick one option for each possible scenario

## Slide 9: Issue with SSB SCS in mixed numerology
UE behavior for measurements and Network configuration should be clarified for UE’s that declare mixed numerology support in the following scenario
  carrierBandwidth > 50 MHz, SSB SCS 15kHz
WF: companies are encouraged to clarify if there are issues in above scenario

## Slide 10: For information only (not for approval)
  For Network
    Explore if the network will deploy this scenario
      carrierBandwidth > 50 MHz with SCS >15kHz, SSB SCS 15 kHz
  For UE side
    For UE with mixed numerology capability between simultaneous receiving data and SSB, UE behaviour needs to be clarified whether UE needs to support the above scenario with or without measurement gaps
Alt1:CC BW1(>50MHz), SCS=30K
SSB SCS=15K
SSB SCS=15K
Alt 2: CC BW2(<=50MHz), SCS=30K
Network configuration Alt 1
Network configuration Alt 2