## Slide 1: WF on Pcmax Inter-Band EN-DC requirement
3GPP TSG-RAN WG4 Meeting #88bis R4-1814168 ChengDu, CN, 8 - 12 October 2018
InterDigital

## Slide 2: Background
The progress made in meeting #88bis has been captured in the draft CR in R4-1813844 from Qualcomm
The main achievements that have to be preserved in further discussions are presented in the next slide.

## Slide 3: Progress made in meeting 88Bis for inter-band EN-DC - Pcmax
The progress made in meeting #88bis has been captured in the draft CR in R4-183844 from Qualcomm built on R4-1811484 (as mandated by RAN plenary in RP-182034).
The main achievements for inter-band EN-DC Pcmax that have to be preserved in further discussions are:
1. The total configured transmission power for both synchronous and non-synchronous operation is
  P_EN-DC_Total = MIN { PEMAX, EN-DC ,PPowerClass, EN-DC}
  P_EN-DC_Total is the dB value of , which is used in [38.213] and PEMAX, EN-DC is p-maxUE-FR1-r15 value signaled by RRC and defined in [36.331];
2. The use in the “IF Conditions” for Pcmax_EN_DC_L determination of the real Pcmax_LTE and Pcmax_NR
3. The X_scale value is the scaling against the real Pcmax_NR in the IF conditions.

## Slide 4: Way Forward
Use the draft CR in R4-1813844 from Qualcomm as a baseline for further proposals, preserving the achieved agreements in meeting #88bis.
The companies are encouraged to bring test cases design for inter-band EN-DC that will show:
  How the current baseline can be tested(including GCF style of test – the flow and how parameters are used and results validated).
  Any problem with the current baseline CR in R4-1813844
For any CR improvement should be justified and it would be required to show the delta with the current baseline by numerical examples and also how this can be tested.