## Slide 1: Dual SMTC Way Forward
Ericsson
3GPP TSG-RAN WG4 RAN#88 Bis
Chengdu, China, 8th- 12th October, 2018
R4-1814214
Document for: Approval

## Slide 2: Background
For intra-frequency measurement objects, dual SMTC periodicities may be configured
  SMTC2 for cells with explicitly listed physical cell ID(PCI)
  SMTC1 for cells without explicitly listed PCI
SMTC2 period < SMTC 1 period
Inter-frequency measurement objects are always configured with a single SMTC periodicity
RAN4 needs to investigate the impact on requirements

## Slide 3: Way forward
In RAN4#88bis, the focus shall be on completing work assuming single intra-frequency SMTC for scaling factors for requirements for
  measurement objects measured within gaps (eg CSSFwithin_gap,i ) including measurement gap sharing with inter-frequency/interRAT measurement objects
  Intra frequency Measurement objects measured outside gaps (eg CSSFoutside_gap,i) including measurements with one or more Scells.
For RAN4#89, companies are invited to provide input on how the agreements for single SMTC may be extended to cover the case of dual intra-frequency SMTC.
Four scenarios are provided for further evaluation. Investigation of other scenarios is not precluded

## Slide 4: Scenarios for evaluation of dual SMTC
Scenario 1 : UE performs type A/B measurement with dual SMTC completely outside of measurement gap pattern (eg no measurement gaps are configured)
Scenario 2 : Measurement gaps are configured such that the gaps are fully overlapping with type A/B measurement for both SMTC1 and SMTC2
Scenario 3 : Measurement gaps are configured such that they are fully overlapping with SMTC1 and partially overlapping with SMTC2
Scenario 4 : Type C measurement is configured with dual SMTC. Other type D measurements may also be configured.

## Slide 5: Annex : Definition of measurement types
R4-1801829, “Way forward on UE measurement gap for NR” defines the following measurement types:
  RLM
  Measurement type A: Intra-frequency measurement w/o MG and w/o interruption
    For FR1, no mixed numerologies is assumed for this measurement type
    For FR2, this measurement type is not applicable
  Measurement type B: intra-frequency measurement with interruption
    For FR1, mixed numerologies is assumed for this measurement type
    For FR2, Rx beam sweeping is assumed for this measurement type
  Measurement type C: intra-frequency measurement with MG
    E.g. Intra-frequency measurement outside active BWP
  Measurement type D: inter-frequency measurement and inter-RAT measurement