## Slide 1: Way forward on NR PBCH demodulation requirements
CMCC, Huawei, HiSilicon, China Telecom, ZTE, CATT, NTT DOCOMO, Vodafone, Orange, Sprint, KDDI, SoftBank
3GPP TSG-RAN WG4 Meeting #88Bis R4-1814240
Chengdu, China, 08 - 12 October 2018
Agenda Item: 7.13.1.3

## Slide 2: Agreements
RAN4 introduces 2Rx PBCH demodulation requirements in Rel-15.
FFS whether to introduce 4Rx PBCH requirements in Rel-15
  If 4Rx PBCH requirements is introduced,
    whether to apply 4Rx PBCH requirements is up to UE declaration
    Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements. (i.e. no conformance requirements)
  Decision should be made in November meeting
Test metric:
  SNR_PBCH@1% Pm-bch. Pm-bch is defined as 1-A/B, where A is the number of correctly decoded MIB PDUs and B is the number of transmitted MIB PDUs.
  UE combines the PBCH symbols of the same SSB index within the MIB TTI (80ms).
Interested companies are encouraged to provide the simulation results in RAN4#89.

## Slide 3: Simulation assumptions
Parameters | Unit | Value
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including 24 bits CRC and 8 bits of SS/PBCH location information) | bits | 56
Receiver assumption |  | LMMSE
Table 1: common parameters
For PBCH demodulation requirements
  The simulation assumptions in Table 1 are subject to common setup
  The simulation assumptions in Table 2 are subject to alignment purpose

## Slide 4: Simulation assumptions
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency Range | FR1 | FR1 | FR2 | FR2
Channel Bandwidth | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 1) | Case A | Case B Case C | Case D | Case E
Antenna Configuration (Note 2) | 1x2 1x4 | 1x2 1x4 | 1x2 | 1x2
Propagation channel (Note 2) | TDL-C RMS DS=300ns Doppler=100Hz | TDL-A RMS DS=30ns, Doppler=10Hz | TDL-A RMS DS=30ns, Doppler=300Hz | TDL-A RMS DS=30ns, Doppler=75Hz
Table 2: Test cases for PBCH demodulation
Note 1: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern
Note 2: Use PDP specified in TS38.901

## Slide 5: Way forward
RAN4 further study in RAN4#89 :
  the PBCH demodulation performance with/without the knowledge of SSB index (or PBCH DMRS sequence).
  PBCH demodulation requirements consider SSB index acquisition performance or not.