## Slide 1: Way forward on MRTD and MTTD for inter-band NR CA between FR1 and FR2
Ericsson, CATT, T-Mobile Inc., ZTE, Nokia, Nokia Shanghai Bell, Verizon, AT&T, Vodafone, Orange, NTT Docomo Inc., Deutsche Telekom, Telecom Italia, …
3GPP TSG-RAN4 Meeting #89
Spokane, Washington, USA, 12-16 November 2018
R4-1815649

## Slide 2: Background
MRTD and MTTD for inter-band NR CA between FR1 and FR2 is still open.
  MRTD is directly related to allowed deployment flexibility for the operators
A number of proposals for MRTD have been available in past meetings
  33µs: Corresponds to 30µs of relative propagation delay difference and 3µs of BS TAE
    R4-1811711, Way forward on MRTD and MTTD for inter-band NR CA between FR1 and FR2, Ericsson, Nokia, ZTE, CATT, Verizon, KDDI, Vodafone, AT&T, Orange, T-Mobile Inc., NTT Docomo Inc.
    R4-1812700, Discussion on MRTD and MTTD in inter-band NR CA, Nokia, Nokia Shanghai Bell
    R4-1812255, CR on MTTD and MRTD for inter-band CA, CATT
  16µs: Corresponds to 13µs of relative propagation delay difference and 3µs of BS TAE
    R4-1813489, MRTD and MTTD Requirements for Inter-band FR1-FR2 NR CA, Qualcomm
  25µs: Corresponds to 22µs of relative propagation delay difference and 3µs of BS TAE
    R4-1815648, Further discussions on FR1-FR2 inter-band NR CA MRTD requirements, Ericsson

## Slide 3: A compromise proposal
For inter-band FR1-FR2 NR CA operation,
  the UE shall be capable of handling at least a relative receive timing difference (MRTD) between slot timing of different carriers to be aggregated at the UE receiver of 25µs.
  the UE shall be capable of handling at least a relative transmit timing difference (MTTD) between slot timing of different carriers to be aggregated at the UE transmitter of 26.1µs.