## Slide 1: Wayforward on UE Rx beam switch under FR2 intra-band NCCA MRTD
Mediatek
3GPP TSG-RAN WG4 RAN#89
Spokane, USA, 12th- 16th November, 2018
R4-1816126
Document for: Approval

## Slide 2: Background
Current MRTD requirement of FR2 intra-band NCCA in Table 7.6.4-1 in TS38.133 is 3us
CP lengths is shorter than MRTD requirement of FR2 intra-band NCCA
  1.17us for SCS 60KHz
  0.59us for SCS 120KHz
  0.295us for SCS 240KHz
Table 7.6.4-1: Maximum receive timing difference requirement for intra-band non-contiguous NR carrier aggregation
Frequency Range | Maximum receive timing difference (µs)
FR1 | 3
FR2 | 3

## Slide 3: Background
In case the receive timing difference of 2 serving cells is larger than CP, UE can find nowhere to switch its Rx beam without degrading the reception performance
  An example is provided below for illustration
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
sym
cp
CC#1 DL
CC#2 DL
Slot to be received with Rx beam 2
Slot to be received with Rx beam 2
Slot to be received with Rx beam1
Slot to be received with Rx beam1
MRTD: 3us

## Slide 4: Wayforward
RAN4 to discuss how to deal with the impact of 3us MRTD to UE’s Rx beam sweeping in R4#90 meeting. Possible options are listed below
  Option1: Reduce MRTD requirement from 3 us to X ns
  Option2: Add additional scheduling restriction when TCI-state changes,
    UE can skip one symbol/slot immediately when UE is changing Rx beam
    It is FFS the time location where UE switches Rx beam
  Others options are not precluded.