## Slide 1: Way forward on CA channel spacing
Ericsson, [...]
R4-1902226
3GPP TSG-RAN WG4 Meeting #90
Athens, Greece, 25 February – 1 March, 2019

## Slide 2: Background
LTE CA spacing was devised to
  allow a symmetric UE internal guard band for unequal channel bandwidth
  align with the BS MSR specification
  allow implementations with a common FFT
NR CA and EN-DC channel spacing (current version of spec)
  depends on channel raster, some bands have got more than one raster
  depends on the SCS configured on the adjacent carriers
  the definition of non-contiguous CA depends on the channel raster (can be more than one) and the SCS configured on each CC

## Slide 3: Problems for CA and EN-DC
CA
The defintion of ”non-contiguous” CA is ambiguous, depends on raster and SCS on the carriers
What if the CCs are on different channel rasters?
Requirements apply for each nominal CA channel spacing
  Multiple sets of requirements (can be acceptable; for LAA two nominal spacings are used)
EN-DC
Same as for CA
The CCs on different raster: for e.g. Band 41 + Band n41
  100 kHz raster not specified for Bn41, B41 carriers are on a 100 kHz raster

## Slide 4: Related problem (R4-1901838)
R4-1901838 on a different topic but identifies an additional issue: where is the UE carrier frequency (raster position)?

## Slide 5: Way forward
CA carrier spacing:
Consider adoption of the Proposal 1 in R4-1900583: one single nominal spacing applying for all channel rasters
  FR1
  FR2
Only one set of requirements for all rasters and SCS
Other methods are not precluded
EN-DC carrier spacing:
The same method can be applied but further consideration is needed
for bands with multiple rasters (e.g. Band 41/n41), the proposal above needs amendment in case not all rasters are SCS based
On the ”related” problem (R4-1901838): how to define the UE raster point if the UE bandwidth not equal to BS bandwidth requires further consideration