## Slide 1: Way forward on NR UE CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting RAN4#90 R4-19xxxxx
Athens, Greece, 24th Feb – 1 March 2019

## Slide 2: Agreed test cases list (Background information)
Static CQI test cases (Periodic)
  Test 1.1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 1.2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 1.3: FR2 TDD 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 2.1: FR1 FDD 10MHz &15kHz , 2*2, 2*4 (periodic)
  Test 2.2: FR1 TDD 40MHz&30kHz, 2*2, 2*4 (periodic)
  Test 2.3: FR2 TDD 100MHz& 120kHz, 2*2 (aperiodic)
Sub-band CQI test cases (Periodic)
  Test 3.1: FR1 FDD 10MHz &15kHz
  Test 3.2: FR1 TDD 40MHz&30kHz
Wideband PMI test cases (aperiodic)
  Test 4.1: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 4.2: FR1 TDD 40MHz&30kHz, 4*2, 4*4
  Test 4.3: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 4.4: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 4.5: FR2 TDD 100MHz& 120kHz, 2*2
  Test 4.6: FR2 TDD 100MHz&120kHz, 2*2 with TDD DL-UL pattern DDDSU, S= 12D2G2U
RI test
  Test 5.1: FR1 FDD 10MHz&15kHz, 2*2,4*4 (periodic)
  Test 5.22: FR1 TDD 40MHz&30kHz, 2*2, 4*4 (periodic)
  Test 5.3: FR2 TDD 100MHz&120kHz, 2*2 (aperiodic)

## Slide 3: Test Set-up (1/2)
Issue 1: CS-RS resource/CSI reporting interval and slot offset & minimum CSI delay for aperiodic CSI reporting
  FR1 FDD 15 kHz: 5/1
    For 4Tx wideband PMI test case 4.1, minimum CSI delay 6 ms (6 slots)
    For 8Tx wideband PMI test case 4.3, , minimum CSI delay 8 ms (8 slots)
  FR1 TDD 30 kHz: 10/1
    For 4Tx wideband PMI test case 4.2, minimum CSI delay 5.5 ms (11 slots)
    For 8Tx wideband PMI test case 4.4, minimum CSI delay 6.5 ms (13 slots)

## Slide 4: Test Set-up (2/2)
Issue 2: K1 values
  FR1 FDD 15kHz: [2]
  FR1 TDD 30kHz with TDD DL-UL pattern FR1.30-1: (Aligned with Demodulation test cases)
    [8] if mod(i,10) = 0 [6] if mod(i,10) = 2 [5] if mod(i,10) = 3 [5] if mod(i,10) = 4 [4] if mod(i,10) = 5 [3] if mod(i,10) = 6
    I is slot index per radio frame with 0~19
  FR2 TDD 120kHz with TDD DL-UL pattern FR2.120-2:
    [11] if mod(i,8) = 0 [7] if mod(i,8) = 4 [6] if mod(i,8) = 5 I is slot index per radio frame with 0~79
  FR2 TDD 120kHz with TDD DL-UL pattern FR2.120-1:
    [3] if mod(i,5) = 0 [6] if mod(i,5) = 2 I is slot index per radio frame with 0~79
Notes: Huawei: Need more time check.

## Slide 5: Static CQI test cases
Previous meeting agreements:
  Test SNR points:
    FR1 2Rx FDD:[8/9]dB, [14/15]dB
    FR1 4Rx FDD :[5/6]dB, [11/12]dB
    FR1 2Rx TDD:[8/9]dB, [14/15]dB
    FR1 4Rx TDD :[5/6]dB, [11/12]dB
    FR2 2Rx:[8/9]dB, [14/15]dB
    Other options not excluded
    Include these SNR points into 38.101-4 with [], the SNR points were introduced based on current results from companies; these requirements can be revised based on more results from companies.
Proposals:
  Confirm above agreed SNR points

## Slide 6: Wideband fading CQI test cases
Proposals: Introduce below requirements for wideband CQI test cases
FR2 TDD 2*2 |  |  | 
Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements
[6/7]dB], [12/13] dB | [0.01] | [2%] | [1.05]
FR1 FDD 2*2 |  |  |  | FR1 FDD 2*4 |  |  | 
Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements | Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements
[6/7]dB], [12/13] dB | [0.02] | [20%] | [1.05] | [3/4]dB], [9/10] dB | [0.02] | [5%] | [1.05]
FR1 TDD 2*2 |  |  |  | FR1 TDD 2*4 |  |  | 
Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements | Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements
[6/7]dB], [12/13] dB | [0.02] | [20%] | [1.05] | [3/4]dB], [9/10] dB | [0.02] | [5%] | [1.05]

## Slide 7: Sub-band CQI Test cases
Number of Tx
  Option 1： 1Tx
  Option 2： 2Tx
Decide test points and test requirements in RAN4#90bis based on companies’ results

## Slide 8: PMI test cases
MIMO correlation for FR2 2Tx PMI test case:
  ULA Low
Test requirements (Relative throughput ratio)
  FR1 FDD:
    8T2R, 8T4R: [1.5]
    4T2R,4T4R: [1.3]
  FR1 TDD:
    8T2R, 8T4R: [1.5]
    4T2R,4T4R: [1.3]
  FR2 TDD:
    FR2 TDD FR2.120-2 (DDSU): [1.05]
    FR2 TDD FR2.120-1 (DDDSU):[1.05]

## Slide 9: RI test cases
Test metric:
  a) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 1 shall be ≥ g1;
  b) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 2 shall be ≥ g2;
Test requirements:
  FR1 FDD/TDD 2Rx :
  FR1 FDD/TDD 4Rx:
  FR2 TDD 2Rx:
Test Number | Test 1 (2X2) ULA Low |  | Test 2 (2X2) ULA Low |  | Test 3 (2X2) ULA High for FR1 | 
 | SNR | Gamma 2 | SNR | Gamma 1 | SNR | Gamma 1
 | [0 dB] | [1.0] | [20 dB] | [1.05] | [20 dB] | [0.9]
Test Number | Test 1 (2X4) ULA Low |  | Test 2 (2X4) ULA Low |  | Test 3 (2X4) ULA High for FR1 |  | Test 4 (4X4) ULA Low for FR1 | 
 | SNR | Gamma 2 | SNR | Gamma 1 | SNR | Gamma 1 | SNR | Gamma 2
 | TBD | TBD | [16 dB ] | [1.05 ] | [16 dB ] | [0.9 ] | TBD | TBD
Test Number | Test 1 (2X2) ULA Low |  | Test 2 (2X2) ULA Low |  | Test 3 (2X2) XP High for FR2 | 
 | SNR | Gamma 2 | SNR | Gamma 1 | SNR | Gamma 1
 | [0 dB] | [1.0] | [20 dB] | [1.05] | [20 dB] | [1.05]