## Slide 1: Way forward on NR UE demodulation requirements SNR, Es, Noc and DL power allocation setup
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #90
Athens, Greece, 25 February – 1 March 2019
Agenda Item: 6.14.1.2
R4-1902407

## Slide 2: Background: Side condition emulation modes supported in 38.101-4
Mode 1: Target SNR (SINR) emulation
  Test system transmits desired signal and artificial AWGN in a way to emulate target SNR conditions
  The mode is applicable for the general UE Demodulation and CSI performance requirements
  The Noc power level is selected to ensure that it is far enough above UE RF noise floor to focus on baseband performance verification in the noise-limited environment
  The SNR and Noc power levels shall be specified for each test. The Es power level can be simply derived based on the SNR and Noc levels (Es = SNR + Noc).
Mode 2: Noise free conditions emulation
  Test system transmits desired signal without artificial noise.
  The mode is applicable for the SDR requirements (and potentially for selected UE Demodulation/CSI requirements in the future)
  Es power shall be specified as a per-test parameter.
  Es power level shall be selected in a way to ensure that effective SNR is above certain threshold.

## Slide 3: Way Forward
Issue 1: Noc power level for FR1 Mode 1
  Background: Noc power level for FR1 is in []
  Proposal
    Use a per-band Noc power level
    Noc is at least X dB higher than UE RF noise floor for each band
      Noc (dBm/Hz) = PNoiseRF (dBm/Hz) + X dB
      X value
        Option 1: X = [16 ]dB
      PNoiseRF calculation is FFS and companies are encourage to bring proposals in RAN4 #91

## Slide 4: Way Forward
Issue 2: Es Level for FR1 Mode 2 (only used for Noise free test cases)
  Background: Es power level for FR1 is undefined
  Proposal
    Use per-band Es power level
    Es is at least X dB higher than UE RF noise
      Es (dBm/Hz) = PNoiseRF (dBm/Hz) + X dB
      X value
        Option 1: X = [35] dB
      PNoiseRF calculation is FFS and companies are encourage to bring proposals in RAN4 #91

## Slide 5: Way Forward
Issue 3: Noc for multi-band supporting in FR2 for Mode 1
  Background: “handling of Carrier Aggregation is FFS, and the handling of multi-band relaxation is FFS.””
  AH agreement: For FR2 Noc setup for multi-band devices increase the Noc power level by ΣMBP defined in TS 38.101-2 Table 6.2.1.3-4.
  Proposal: Modify the FR2 Noc equations as follows for multi-band capable devices
Noc(PC_X, Band_Y) = -155 dBm/Hz + RefsensPC_X, Band_Y, 50MHz – RefsensPC3, n260, 50MHz + ΣMBP

## Slide 6: Way Forward
Issue 4: Power allocation setting
  Proposal: Define “EPRE ratio of PBCH/PDCCH/PDSCH to SSS” instead of “EPRE ratio of PBCH_DMRS/PDCCH_DMRS/PDSCH_DMRS to SSS” as follows in Annex C of TS 38.101-4
Parameter | Unit | Value
SSS transmit power | W | Test specific
EPRE ratio of PSS to SSS | dB | 0
EPRE ratio of PBCH to SSS | dB | 0
EPRE ratio of PBCH to PBCH DMRS | dB | 0
EPRE ratio of PDCCH to SSS | dB | 0
EPRE ratio of PDCCH to PDCCH DMRS | dB | 0
EPRE ratio of PDSCH to SSS | dB | 0
EPRE ratio of PDSCH to PDSCH DMRS | dB | Test specific (Note 1)
EPRE ratio of CSI-RS to SSS | dB | 0
EPRE ratio of OCNG to SSS | dB | 0
Note 1: Value is derived from Table 4.1-1 in TS 38.214 [X] based on “Number of DM-RS CDM groups without data” and “DMRS Type” parameters specified for each test |  |