## Slide 1: Way Forward on TCI State Switching Requirements
Intel Corporation,…
3GPP TSG-RAN WG4 Meeting #90bis R4-1904700
Xi’an, China, 8 - 12 April, 2019

## Slide 2: Background
Open Issues for TCI state switching requirements
  Definition of known/unknown TCI state
  MAC CE based TCI state switch for PDCCH
  DCI based TCI state switch for PDSCH
  Requirements for RRC based TCI state switch
  Interruption due to TCI state switch
  TCI for SCell activation (addressed in SCell activation)
  Requirement for MAC-CE based active TCI state list activation

## Slide 3: Way forward on definition of Known TCI state
Agreements
  Definition of known TCI state for UE supporting Power Class 1
    L1-RSRP report made in [x] ms
Open Issues
  Value of x for UE supporting Power Class 1
  Applicability of known/ unknown TCI state for UE supporting Power Class 2/3/4
    Option 1: Only unknown
    Option 2: Both known and unknown

## Slide 4: Way forward on MAC CE based TCI state switch
Agreements
  Definition of switching delay: From the slot with PDSCH carrying the activation command to the slot when PDCCH can be received based on new TCI state
  For UE supporting Power Class 1
    Requirements are defined for known TCI state
    No requirements for unknown TCI state
  Requirement for switching delay for known case: THARQ + 3ms
Open Issues
  Requirements for known/unknown for UE supporting Power Class 2/3/4
    Option 1: Only unknown
    Option 2: known and unknown
  FFS on requirement for unknown case
    The switching delay for unknown case shall include time for L1-RSRP measurement
    It is assumed that the target TCI state remains measureable when TCI state switch is activated

## Slide 5: Way forward on DCI based TCI state switch
Agreements
  Definition of switching delay: From the last symbol of PDCCH to first symbol of PDSCH
  For UE supporting Power Class 1 and Power class 2/3/4
    Requirements are defined for known TCI state
    No requirements for unknown TCI state
  Requirement for switching delay for known TCI state: UE capability for timeDurationForQCL
  In RRM test for DCI based TCI state switch, PDSCH is always scheduled with lowest MCS for new TCI state
Open Issues
  FFS if known case is defined for UE supporting Power Class 2/3/4

## Slide 6: Way forward on RRC based TCI state switch
Open Issues
  If RRC based TCI state switching delay requirements are defined
    Option 1: Yes (DoCoMo)
    Option 2: No (Intel, NEC, Huawei, CATT)

## Slide 7: Way forward on Interruptions for TCI state switch
Agreements
  No interruption allowed due to DCI based TCI switching except for intra-band non-contiguous CA case
  No interruption allowed due to MAC based TCI switching except for intra-band non-contiguous CA case
    Whether to define scheduling restriction requirement for MAC based TCI switching depends on the conclusions for MRTD.
Open Issues
  Interruption due to RRC based TCI state switch if defined
    Option 1: Yes (Intel, QC)
    Option 2: No

## Slide 8: Way forward on MAC CE based active TCI state list update
Background
  Necessity to define delay requirement for MAC CE based active TCI state list update with new TCI state and PDSCH to receive on the newly activated TCI state via DCI based switch
  Assumption that UE has measured and reported L1-RSRP on new TCI state
Open Issues
  Whether requirement for MAC CE based active TCI state list update is introduced
    Option 1: Yes (QC)
    Option 2: No