## Slide 1: WF on NR PUSCH demodulation requirements
R4-1904717
Document for: Approval
3GPP TSG-RAN WG4 RAN#90Bis
Xi’an, China, 8th – 12th April, 2019
Agenda: 6.12.2.2.1
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89
  R4-1902434, WF on NR PUSCH demodulation requirements, RAN4#90

## Slide 3: Reduction of test cases
Removal of test cases with DMRS configuration 1+0
  For FR1, remove all PUSCH test cases with DMRS configuration 1+0 for type A and type B;
Add test applicability rule for test cases with correlation level low
  Option 1:Add the following applicability rule in TS 38.141-1: 8.2.1.2.3 Applicability of requirements for different number of RX antennas Unless otherwise stated, a BS that has declared to support a set of RX antennas for a specific test case, is required to test the lowest and highest numbers of supported RX antennas for which requirements are defined.
  Option 2: No new rule.

## Slide 4: PTRS configuration for MCS2
Background: Agreed applicability rule in R4-1902434:
  “If BS supports both with PT-RS configured and without PT-RS configured, select one of the PUSCH requirements for with PT-RS configured or without PT-RS configured for test, otherwise BS vendor tests the PUSCH requirements for the declared PT-RS configuration supporting.”
Restore balance of test case coverage and consistency by:
  Option 1: Re-introduce previous test cases for MCS 2 with PT-RS enabled.
  Option 2: No change.
  Other options not precluded.

## Slide 5: Test Parameters, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | Full applicable test bandwidth | Full applicable test bandwidth
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5MHz, 10MHz, 20MHz; 30kHz: 10MHz, 20MHz, 40MHz, 100MHz 60kHz(FR2): 50MHz, 100MHz; 120kHz: 50MHz, 100MHz, 200MHz | 
PTRS | Not configured | QPSK: Not configured 16 and 64 QAM: (Configured with KPTRS =2, LPTRS =1) and (not configured, low prio)
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 6: Test Parameters, DFT-s-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1+1, 1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW) | 60kHz: 30 PRB; 120kHz: 30 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz | MCS 2: TDL-A 30ns, 300Hz
SCS and BW | 15kHz: 5 MHz; 30kHz: 10 MHz | 60kHz: 50; 120kHz: 50
PTRS | Not configured | Not configured
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput