## Slide 1: 3GPP TSG-RAN WG4 Meeting #90Bis Xi‘an, China, 04 – 08 April, 2019
Huawei, …
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1904718

## Slide 2: Background
R4-1808025 Way forward on PUCCH demodulation requirements, RAN4#87
R4-1809556 Way forward for NR PUCCH demodulation performance requirements, RAN4#1807
R4-1811727 Way forward for NR PUCCH demodulation performance requirements, RAN4#88
R4-1813943 Way forward on NR PUCCH demodulation requirements, RAN4#88Bis
R4-1816348 Way forward on NR PUCCH demodulation requirements, RAN4#89
RAN4#1902440 Way forward on NR PUCCH demodulation requirements, RAN4#90

## Slide 3: Test Parameters
Capture the test parameters below in TS 38.104, TS 38.141-1 and TS 38.141-2
  pucch-GroupHopping = neither
  hoppingId = 0
  Note: The above two parameters are used for PUCCH format 0, 1, 3 and 4.

## Slide 4: Time Mask for PUCCH
Background
  With the frequency hopping configuration which has been chosen for the demodulation simulation, no additional impairment for the impact of transient period need to be introduced: there is no power change and so no transient period is needed in between symbols.
Agreement
  As per TS 38.101-2 section 6.3.3.1, transient period can be allowed or not
  Add notes in TS 38.104, TS 38.141-2 for FR2 demodulation performance test:
    "Remark: The transient period described in section TDB in TS 38.101-2[X] is not taken into account for minimum performance requirement testing, where the RB hopping is symmetric to the CC center., i.e. intra-slot frequency hopping is enabled"

## Slide 5: UCI on PUCCH
Add note to specify PUCCH UCI demodulation performance requirements do not consider CSI part 2 in specification TS 38.104, 38.141-1 and 38.141-2 for PUCCH formats 2,3 and 4.
Notes: Samsung: consider CSI-1 and CSI-2 are only available for PF2,3 and 4. general for all PUCCH formats.