## Slide 1: WF on CLI measurement
3GPP TSG-RAN WG4 Meeting #90BIS Xian, China, 8 - 12 April 2019
Agenda Item: 8.2.3
R4-1904763
LG Electronics, Ericsson

## Slide 2: Background
Based on objective of WID (RP-190700) for CLI, RAN4 should define SRS-RSRP and CLI-RSSI measurement requirements.
RAN4 needs to clarify remaining issue for SRS-RSRP and CLI-RSSI measurement based on RAN1 agreements.

## Slide 3: Specification structure in TS38.133
Specification structure for CLI WI
  Add subsection in chapter 9 and 10
  Example
9. Measurement Procedure 9.X Cross link interference measurements 9.X.x Introduction 9.X.y SRS-RSRP measurements 9.X.z CLI-RSSI measurements 10. Measurement Performance requirements 10.1 NR measurements 10.1.Y SRS-RSRP accuracy requirements 10.1.Z CLI-RSSI accuracy requirements

## Slide 4: SRS-RSRP measurement
SRS-RSRP measurements resource configuration
  Based on R1-1903835, RAN4 needs to preclude unnecessary configuration parameters from measurement perspective.
Parameter name in specification | Value range (R1-1903835) | Proposed value range
SRS-scs | 15, 30, 60 kHz for FR1 60, 120 kHz for FR2 | 15, 30, 60 kHz for FR1 60, 120 kHz for FR2
nrofSRS-Ports | 1,[2],[4] | 1
transmissionComb | n2 comboffset (0,1), cyclicShift (0,…,7) n4 comboffset (0,..,3), cyclicShift (0,…,11) | n2 comboffset (0,1), cyclicShift (0,…,7) n4 comboffset (0,..,3), cyclicShift (0,…,11)
resourceMapping | startPosition INTEGER (0,…,5) nrofSymbols ENUMERATED {n1,n2,n4} repetitionFactor ENUMERATED {n1,n2,n4} | startPosition INTEGER (0,…,5) nrofSymbols ENUMERATED {n1} repetitionFactor ENUMERATED {n1}
freqDomainPosition | 0,…,67 | 0,…,67
freqDomainShift | 0,…,268 | 0,…,268
freqHopping | c-SRS INTEGER (0,…,63) b-SRS INTEGER (0,…,3) b-hop INTEGER (0,…,3) | no
groupOrSequenceHopping | neither, groupHopping, sequenceHopping | no
SRS-Measurement-PeriodicityAndOffset (only periodic) | sl1 NULL, sl2 INTEGER(0..1), sl4 INTEGER(0..3), sl5 INTEGER(0..4), sl8 INTEGER(0..7), sl10 INTEGER(0..9), sl16 INTEGER(0..15), sl20 INTEGER(0..19), sl32 INTEGER(0..31), sl40 INTEGER(0..39), sl64 INTEGER(0..63), sl80 INTEGER(0..79), sl160 INTEGER(0..159), sl320 INTEGER(0..319), sl640 INTEGER(0..639) | option 1: use all periodicity option 2: reduce periodicity set

## Slide 5: CLI-RSSI measurement
Based on other previous release WI (V2X)
  CLI-RSSI measurement accuracy for CLI is
    not impacted by baseband estimation error
    only considered RF margin

## Slide 6: General measurement
DL Measurement timing error
  RAN1 agreement
    UE is not required to perform time tracking or time adjustment other than a constant offset relative to its own DL timing.
      The constant offset is derived by UE implementation
  RAN4 proposal
    Baseline UE behavior for derivation of constant offset is up to UE implementation
      UE may assume that constant offset value = TA_offset + TA_serving
    Further evaluations for CLI measurement accuracy according to DL measurement timing error are needed
      Companies are encouraged to provide analysis of CLI measurement impact on DL measurement timing error
    Further study the cyclic shift ambiguity due to propagation delay difference of two interfering UEs

## Slide 7: General measurement
QCL assumption
  RAN1 agreement
    QCL assumption on CLI-RSSI and SRS-RSRP interference measurement resources is up to UE implementation
  RAN4 proposal
    Baseline UE behavior for QCL assumption is the same spatial filter/set of UE Rx beams as used for reception of PDCCH and PDSCH on the same carrier
    FFS if other UE behavior needs to be considered

## Slide 8: General measurement
Measurement reporting range
  SRS-RSRP measurement
    Reuse SS-RSRP measurement reporting range (Table 10.1.6.1-1 in TS38.133) as starting point
  CLI-RSSI measurement
    Reuse RSSI measurement reporting range for LAA (Table 9.1.18.5.1-1 in TS36.133) as starting point