## Slide 1: Way forward on L1-RSRP accuracy requirements
Ericsson, Nokia, CMCC
3GPP TSG-RAN WG4 Meeting #90bis
Xi’an, China, 8 – 12 April, 2019
R4-1904820

## Slide 2: Agreements
The CSI-RS based L1-RSRP accuracy requirements are defined based on 48PRB.
  Clarify in the spec that the performance with larger bandwidth is equal to or better than the accuracy based on 48PRB.
  The requirement for larger or lower bandwidth will be further discussed in the future release.

## Slide 3: Summary of alignment simulation results (R4-1904760)
RS | SCS | PRB |  | Ericsson | CMCC | Huawei | Nokia | MediaTek | Intel | 
 |  |  |  | R4-1903892 | R4-1903441 | R4-1903768 R4-1901173 | R4-1903919 | R4-1903592 | R4-1903402 | Average
SSB | 15kHz |  | max(5%, 95%) | 1.2 |  | 1.09 | 1.61 | 1.4 | 2.67 | 1.6
 | 30kHz |  | max(5%, 95%) | 0.8 |  | 1.13 | 1.59 | 1.38 | 2.76 | 1.5
CSI-RS | 15kHz | 48 | max(5%, 95%) | 0.77 | 1.77 | 1.18 | 1.51 | 1.84 | 2.43 | 1.6
 | 30kHz | 48 | max(5%, 95%) | 0.55 | 1.71 | 1.04 | 1.49 | 1.78 | 2.44 | 1.5
RS | SCS | PRB |  | Ericsson | CMCC | Huawei | Nokia | MediaTek | Intel | 
 |  |  |  | R4-1903892 | R4-1903441 | R4-1903768 R4-1901173 | R4-1903920 | R4-1903592 | R4-1903402 | Average
SSB | 120kHz |  | max(5%, 95%) | 0.35 |  | 1.09 | 1.61 | 1.49 | 2.85 | 1.5
CSI-RS | 120kHz | 48 | max(5%, 95%) | 0.28 |  | 1.14 | 1.49 | 1.82 | 2.56 | 1.5

## Slide 4: L1-RSRP accuracy for FR1
Relative accuracy requirements
  Considering fading condition (+1.0dB) and reporting step size of 1dB for absolute reporting and 2dB for differential reporting
Absolute accuracy requirements
  Normal condition with Io=-70dBm/BW is derived by adding 1.0dB (fading) + 2.5dB (RF margin) to the average of alignment results (1.5dB). => 1.5+2.5+1.0 = [+/-5.0]dB
  Extreme condition with Io=-70dBm/BW is derived by adding 4.5dB to the absolute L1-RSRP accuracy in normal condition.
  Normal condition with Io=-50dBm/BW is derived by adding 3.5dB to the absolute L1-RSRP accuracy in normal condition with Io=-70dBm/BW.
  Extreme condition with Io=-50dBm/BW is derived by adding 2dB to the absolute L1-RSRP accuracy in extreme condition with Io=-70dBm/BW.
 | Normal condition | Extreme condition
SSB based relative L1-RSRP | [+/-3.0]dB | [+/-4.0]dB
CSI-RS based relative L1-RSRP | [+/-3.0]dB | [+/-4.0]dB

## Slide 5: L1-RSRP accuracy for FR2
Relative accuracy requirements
  Considering fading condition (+1.0dB), RF margin for FR2 (+4.0dB)
Absolute accuracy requirements
  Normal condition with Io=-70dBm/BW is same as the relative accuracy of normal condition because FR2 cannot compensate the RF impairments, i.e., [+/-6.5]dB
  Extreme condition with Io=-70dBm/BW is derived by adding 3dB to the absolute L1-RSRP accuracy in normal condition.
  Normal condition with Io=-50dBm/BW is derived by adding 2dB to the absolute L1-RSRP accuracy in normal condition with Io=-70dBm/BW.
  Extreme condition with Io=-50dBm/BW is derived by adding 2dB to the absolute L1-RSRP accuracy in extreme condition with Io=-70dBm/BW.
 | Normal condition | Extreme condition
SSB based relative L1-RSRP | [+/-6.5]dB | [+/-9.5]dB
CSI-RS based relative L1-RSRP | [+/-6.5]dB | [+/-9.5]dB