## Slide 1: WF on RefSens exceptions due to UL harmonic for SA CA and EN-DC
vivo, Mediatek, Skyworks
3GPP TSG-RAN WG4#90bis Meeting R4-1904980
Xi’an, China, 8th - 12th April, 2019

## Slide 2: Background (1)
In Rel-12 LTE, the Reference sensitivity exceptions due to UL harmonic interference, MSD value and scheme were developed for CA_3A-42A.
Channel conditions for MSD study.[R4-147285]
3400 MHz
3600 MHz
MSD B
20 MHz CBW
15 MHz CBW
10 MHz CBW
5 MHz CBW
Channel where 2nd harmonic directly hits. They are 5, 10, 15 and 20 MHz
Offset: [10] MHz
Channels where 2nd harmonic does not directly hits.
MSD A
MSD B

## Slide 3: Background (2)
Further explanation from [R4-148024][R4-147741]
CR agreed in [R4-150441].

## Slide 4: Background (3)
For NR SA CA and EN-DC, the same set of MSD scheme and values were reused for a number of combinations, with the victim band n77/n78 with 2nd order harmonic interference
Some of the UL allocation was consistent while some are not:
  Consistent: Harmonics are always inside the victim receive bandwidth to measure the larger MSD for direct hit. These are applied to victim channel bandwidth
  In-consistent: UL allocation of aggressor was enlarged for certain band combination.
Location of the allocated RBs within the aggressor channel are not clear for some case.

## Slide 5: Way Forward (1)
Proposal 1:Keep the channel conditions for the band combinations which use the same MSD scheme and values with CA_3A-42A
  UL restriction 50 RB for > 20MHz DL channel bandwidth in victim high band
  UL RB allocation number independent of UL aggressor channel bandwidth
  The offset equation for lower MSD region would not be impacted.

## Slide 6: Way Forward (2)
Proposal 2: Clarify that unless stated otherwise, UL resource blocks shall be centred within the transmission bandwidth configuration for the channel bandwidth.
  This configuration is defined for combinations with direct overlap.
  For combinations with no direct overlap, the uplink configuration and allocation would be defined case by case.

## Slide 7: Reference
[1] R4-1904658, Discussion on MSD requirements applicability for CA_n3A-n78A and DC_3C_78A, RAN4#90bis
[2] R4-1904978, Correction of RefSens exceptions due to UL harmonic interference for NR CA in 38.101-1
[3] Correction of RefSens exceptions due to UL harmonic interference for EN-DC in 38.101-3