## Slide 1: WF on coexistence of NB-IoT with NR
Huawei, HiSilicon, Ericsson, Nokia,
ZTE, DISH, T-Mobile USA, CHTTL
3GPP TSG-RAN WG4 Meeting#91
Reno, USA, May 13th – 17th 2019
R4-1907809

## Slide 2: Agreements
Agreements on NB-IoT operation in NR guard band
  Considering legacy deployments, even if one NB-IoT 15 kHz sub-carrier would operate in NR guard band, still consider this case as NB-IoT operation in NR in-band.
  NB-IoT operating in NR guard band is handled as implementation issue and RF requirements are not specified in Rel-15 (nor in Rel-16 unless new Rel-16 features make this essential).
  Define in-band, guard band and standalone operation with NR.
WF on Power Boosting:
  Option 1:
    For 5 MHz channel bandwidth, specify the same +6 dB power boosting requirement for in-band 25 RB.
    For 10 MHz channel bandwidth, specify the same +6 dB power boosting requirement for in-band 52 RB.
    For 15 MHz channel bandwidth, specify the same +6 dB power boosting requirement for in-band center 77 RB.
    For 20 MHz channel bandwidth, specify the same +6 dB power boosting requirement for in-band center 102 RB
    (Single/multiple) declaration(s) on other RBs on the edge for the 15/20 MHz channel bandwidth.
    FFS on other channel bandwidth>20 MHz
  Option 2:
    +6 dB power boosting shall be supported for any NR channel bandwidth and NB-IoT RB position.
Agreements on TDD
  Conclusion: NB-IoT could operate in NR TDD by choosing suitable UL-DL configuration(s).
  ZTE/Ericsson to provide TP to TR in next meeting

## Slide 3: Agreements on operations and Testability
  MSR BS supporting NR and LTE+NB-IoT (LTE in-band/guard band) should also meet current RF requirements when operating NR+(LTE)+NB-IoT (NR in-band) with following limitations:
    Same NR channel bandwidth as LTE
    NR uses 15 kHz SCS
    NB-IoT carrier frequency kept when operating with LTE and NR, or shifted closer to NR carrier.
  Therefore:
    MSR BS could operate NB-IoT in NR in-band with above limitations.
    No need to redo conformance testing in this case.
To remove any limitation:
    Add support for NB-IoT operating in NR in-band in TS 38.104, TS 38.141-1 and TS 37.141
    Rel-15 NR BS can declare to support Rel-16 NB-IoT RF requirements for NB-IoT coexistence with NR.

## Slide 4: FFS
TAGs misalignment

## Slide 5: References
R4-1905565 Clarification on NB-IoT operation modes Huawei, HiSilicon
R4-1905566 TP for NB-IoT standalone operating Huawei
R4-1905567 NB-IoT operating in NR guard band Huawei, HiSilicon
R4-1905568 Discussion on power boosting Huawei, HiSilicon
R4-1905982 NB-IoT - NR coexistence : TP to TR - channel raster Ericsson, ZTE
R4-1905983 NB-IoT - NR coexistence : System scenarios considerations Ericsson
R4-1905984 NB-IoT - NR coexistence : TDD synchronization considerations Ericsson
R4-1905985 NB-IoT - NR coexistence : Testability considerations Ericsson
R4-1905986 NB-IoT - NR coexistence : Power boosting considerations Ericsson
R4-1906385 Considerations on NB-IoT/NR Co-existence Dish Network
R4-1906586 Further aspects on coexistence scenarios between 15kHz SCS NR and in-band NB-IoT CHTTL
R4-1906587 Discussion on the operating scenarios for NB-IoT with NR in-band/guard band CHTTL
R4-1906597 TP to the new TR related to NB-IoT: mixed numerologies ZTE Corporation
R4-1906604 Discussion on NR and NB-IoT coexistence ZTE Corporation
R4-1906924 System level simulation results for uplink coexistence study between R15 NR and R13/R14/R15 NB-IoT standalone operation Nokia, Nokia Shanghai Bell
R4-1906925 System level simulation results for uplink coexistence study between R15 NR and R13/R14/R15 NB-IoT standalone operation (with NR channel model) Nokia, Nokia Shanghai Bell
R4-1906926 TP to TR38.xxx: Summary of system level simulation results for coexistence study between R15 NR and R13/R14/R15 NB-IoT standalone operation Nokia, Nokia Shanghai Bell
R4-1906927 Proposals on definitions of in-band, guard band and stand-alone operations when NB-IoT is located within NR channel bandwidth Nokia, Nokia Shanghai Bell
R4-1906928 Proposals on power boosting requirement when NB-IoT is located within NR channel bandwidth Nokia, Nokia Shanghai Bell