## Slide 1: WF on NR-U 6 GHz band plan
Qualcomm Incorporated
R4-1907963
3GPP TSG-RAN WG4 #92
August 26th – 30th, 2019
Ljubljana, SI

## Slide 2: Background
WID objective
  “This work item will specify NR enhancements for a single global solution framework for access to unlicensed spectrum which enables operation of NR in the 5GHz and the 6GHz (e.g., US 5925 – 7125 MHz, or European 5925 – 6425 MHz, or parts thereof) unlicensed bands taking into account regional regulatory requirements. The core technology should be band agnostic as much as possible.” [1]
Regulatory uncertainty
  Regulations have not been finalized in Europe or US for unlicensed usage in the 6 GHz frequency range.
  Regulations are not expected to be finalized until mid-2020, after completion of the WI.
RAN plenary guidance on prioritization
  In [2], it was agreed that band plan definition work for 6 GHz band is prioritized. It is regarded as an essential element of the WID.

## Slide 3: Way forward
RAN4 to define two bands in 6 GHz for NR-U
  Band X: 5925 – 6425 MHz (Europe focused)
  Band Y: 5925 – 7125 MHz (US focused)
  These two bands meet the objectives of the WID and the guidance from RAN to define a band plan in 6 GHz
Define only the generic RF requirements
  Until regulations are complete, it is difficult to fully define all deployment-specific requirements (i.e., emissions levels, PSD restrictions, etc)
  It is FFS whether generic requirements developed for 5 GHz NR-U band (Band n46) can suffice for 6 GHz band as well
Deployment-specific requirements are added as future NS
  Regulatory requirements such as emission limits, PSD restrictions and their associated A-MPR would be defined under a future NS (possibly multiple)
  Requires multiple NS signaling capability to be available
  LS is sent to RAN2 to request enabling multiple NS signaling for NR

## Slide 4: References
[1] RP-191575, “Revised WID on NR-based Access to Unlicensed Spectrum,” Qualcomm Inc.
[2] RP-191581, “Guidance on essential functionality for NR-U,” Qualcomm