## Slide 1: Way forward on NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #92
Ljubljana, SI, 26 – 30 Aug, 2019
R4-1908234
Document for: Approval

## Slide 2: Feasibility of handover with simultaneous Rx/Tx with source and target cells
Interband HO with simultaneous Rx/Tx with source and target cells supports different SCS to be configured for source and target cell.
FFS on whether or not interfrequency intraband HO with simultaneous Rx/Tx with source and target cells supports different SCS to be configured for source and target cell
FFS on whether or not intrafrequency HO with simultaneous Rx/Tx with source and target cells supports different SCS to be configured for source and target cell

## Slide 3: Handover delay of handover with simultaneous Rx/Tx with source and target cells
The legacy handover delay definition may not be suitable for simultaneous connectivity handover.
The starting point of handover delay is defined as the time when UE receives RRC indicating handover. The ending point of handover delay is FFS.
RAN4 needs to discuss if delay and interruption requirement is needed for source cell release.

## Slide 4: Agreements on conditional handover
Conditional handover does not add additional monitoring frequency layers, cells, and SSBs on top of existing Rel-15 UE measurement capability.
How to capture this in TS38.133 is FFS (if needed)
The definition of when the CHO delay starts is FFS
Exact delay equation is FFS
UE RRC processing time is broken into two segments:
First segment is immediately after RRC HO command reception
Second segment is after UE realizes the condition is met and identity of target cell is determined